## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Prof. Peter Edwards
p.edwards@abdn.ac.uk
Notes: Some slides in this set adapted from:
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2: Transistors

## Slide 3: Transistor
A semiconductor device that amplifies, oscillates, or switches flow of current between two terminals by varying the current or voltage between one of the terminals and a third.
Most common types:
  Bipolar Junction Transistor (BJT)
  Field-Effect Transistor (FET)
Logic gates can be built from transistors.
Notes: Most common FET is metal–oxide–semiconductor FET (MOSFET) – dominates ICs (integrated circuit)
There are two types of transistors, which have slight differences in how they are used in a circuit.

## Slide 4: Bipolar vs Field-Effect Transistors
Bipolar Junction (BJT)
  Terminals labeled base, collector, emitter
  small current at the base can control or switch a much larger current between the collector and emitter.
Field-Effect (FET)
  Terminals labeled gate, source, drain
  voltage at the gate can control a current between source and drain.
Notes: BJT image is for a PNP device
FET image is for a p-channel device (actually pMOS)

## Slide 5: World’s First Transistor
December 23, 1947
AT&T Bell Labs, USA
John Bardeen, William Shockley & Walter Brattain
Notes: Actually what Bardeen, Brattain, and Shockley invented in 1947 was the first point-contact transistor.
Transistor Effect “when electrical contacts were applied to a crystal of germanium, the output power was larger than the input.”
Shockley, Bardeen, and Brattain were jointly awarded the 1956 Nobel Prize in Physics "for their researches on semiconductors and their discovery of the transistor effect.”
The first working silicon transistor was developed at Bell Labs on January 26, 1954 by Morris Tanenbaum.
The first commercial silicon transistor was produced by Texas Instruments in 1954

## Slide 6: Silicon Transistors
Transistors most commonly built from silicon (Group IV)
Pure silicon is a poor conductor (no free charges)
Doped silicon is a good conductor (free charges)
  n-type (free negative charges, electrons)
  p-type (missing electrons, holes)
Junction between p- and n-type semiconductors – crucial to their function.
Notes: Silicon is discussed here as the most common semiconductor material used to date.
NB Materials used and date of first usage: germanium (1947), silicon (1954), gallium arsenide (1966) and silicon carbide (1997), the alloy silicon-germanium (1989), graphene (research ongoing since 2004)
Doping: Process of introducing impure elements (dopants) into semiconductor wafers to form regions of differing electrical conductivity
P-type semiconductors
  Created positive charges, where electrons have been removed, in lattice structure
N-type semiconductors
  Added unbound electrons create negative charge in lattice structure
Resulting material
  P-N junction
A P-N junction between p-type and n-type semiconductor forms a diode.
Current flows only in one direction.

## Slide 7: MOS Transistors
Metal oxide silicon (MOS) transistors
Four terminals: gate, source, drain, body*
Gate – oxide – body stack looks like a capacitor
Gate and body are conductors
SiO2 (oxide) is a very good insulator
* - body is usually tied to the source – giving a 3 terminal device.
Notes: Type of FET
Metal oxide silicon - Even though gate is no longer made of metal*
CMOS - Complementary metal–oxide–semiconductor

## Slide 8: MOS Operation
Gate at a low voltage:
  P-type body is at low voltage
  Source-body and drain-body diodes are OFF
  No current flows, transistor is OFF
Gate at a high voltage:
  Negative charge attracted to body
  Inverts a channel under gate to n-type
  Now current can flow through n-type silicon from source through channel to drain, transistor is ON

## Slide 9: pMOS Transistors
Similar to MOS, but doping and voltages reversed
Body tied to high voltage (VDD)
Gate low: transistor ON
Gate high: transistor OFF
Bubble indicates inverted behavior

## Slide 10: Transistors as Switches
3-ported voltage-controlled switch
  2 ports connected depending on voltage of 3rd

## Slide 11: Realising a CMOS NOT Gate
A | Y
0 | 1
1 | 0
P1
N1
A | P1 | N1 | Y
0 | ON | OFF | 1
1 | OFF | ON | 0
Notes: Two important characteristics of CMOS devices are high noise immunity and low static power consumption.
Why C MOS?
complementary refers to the fact that the typical design style with CMOS uses complementary and symmetrical pairs of p-type and n-type MOS transistors (MOSFETs) for logic functions
Commercial CMOS products are integrated circuits composed of up to billions of transistors of both types, on a rectangular piece of silicon of between 10 and 400 mm2.

## Slide 12: Realising a CMOS NAND Gate
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 1
1 | 0 | OFF | ON | ON | OFF | 1
1 | 1 | OFF | OFF | ON | ON | 0
Notes: P1 and P2 in parallel – so only one needs to be ON for Y to ‘lift’ to VDD (1)
N1 and N2 in series – so both need to be ON to drop Y to GND (0)

## Slide 13: Realising a CMOS NOR Gate
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
P1
P2
N1
N2
A | B | P1 | P2 | N1 | N2 | Y
0 | 0 | ON | ON | OFF | OFF | 1
0 | 1 | ON | OFF | OFF | ON | 0
1 | 0 | OFF | ON | ON | OFF | 0
1 | 1 | OFF | OFF | ON | ON | 0
Y = A + B

## Slide 14: A 3-Input NOR Gate