## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Assembly Language
8086 Instruction Set
Part 1

## Slide 2: sign numbers
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign representations of ± 6:
  +6 =?
  - 6 =?

## Slide 3: sign numbers
1 sign bit, N-1 magnitude bits
Sign bit is the most significant (left-most) bit
  Positive number: sign bit = 0
  Negative number: sign bit = 1
Example, 4-bit sign representations of ± 6:
  +6 =0110
  - 6 =1110

## Slide 4
Problems:
  Addition doesn’t work, for example -6 + 6:
1110
+ 0110
10100 (wrong!)
  Two representations of 0 (± 0):
1000
0000

## Slide 5: Two’s complement
use a sign bit as an indicator of the sign of the number
+ve number: the representation is identical to that of signed magnitude. The sign bit is 0 and the remaining bits represent the positive number
-ve number: the sign bit is 1, but the bits to the right of the sign bit do not directly indicate the magnitude of the number

## Slide 6
1000 1101 1110 1111 0000 0001 0010 0011
-4 -3 -2 -1 0 +1 +2 +3
4-bit two’s complement numbers with their decimal equivalents
The following shows the range of numbers that can be represented using a 4-bit two’s complement representation.

## Slide 7: Two’s complement
to negate a number to 2’s complement: Flip the bits and add 1
  8910 = 01011001
  one’s complement 8910 = 10100110
  add one +1
  Two’s complement -8910 = 10100111

## Slide 8: 8086 Instruction Set
over 120 instructions in 8086
four main groups:
  data manipulation
  arithmetic and logical
  I/O instructions
  transfer-of-control

## Slide 9: mov Instruction
transfer data between registers or between memory and registers
not transfer data from one memory variable to another in a single mov instruction
mov destination, source

## Slide 10: mov Instruction example
mov ax, 2
mov cx, ax
mov x, ax ;x is a memory variable
mov dx, y
mov bx, ‘a’
mov dl, ‘?’
0000 0000 0000 0010
0000 0000 0000 0010
ax
cx
mov cx, ax

## Slide 11
what is their difference?
mov dl, 3
mov dx, 3

## Slide 12
mov dl, 3
  (only dl register changed, dh register unchanged by mov instruction)
mov dx, 3
(the entire dx register changed, dl stores 03h, dh stores 00h

## Slide 13: Arithmetic Instructions - mul
the destination operand of add, inc, dec, sub instructions must be a storage location, either a register or memory location
mul instruction takes a single operand, the other operand must be the ax or al
when two 8-bit numbers are multiplied, the result will be stored in ax register
when two 16-bit numbers are multiplied, the result will be in the pair of register dx:ax (ax containing the low-order bits; dx contains the high-order bits)

## Slide 14: Arithmetic Instructions - mul example
Multiply 7 by 9:
mov al, 7
mov bl, 9
mul bl ; ax=al*bl = 63
note that mul instruction takes a single operand, and the al (ax) register is implicitly used for the second operand

## Slide 15: Arithmetic Instructions - div
divide an 8-bit number into a 16-bit number (byte division)
  the number to be divided must be stored in the ax register and the divisor may be in another register or memory location
divide an 16-bit number into a 32-bit number (word division)
  the 32-bit number must be stored in 2 registers: bx and ax registers

## Slide 16: Arithmetic Instructions - div example
Divide 1235 by 10:
mov ax, 1235
mov cl, 10
div cl
; divide ax by 10, al now contains 123 and ah contains 5
the div instruction takes a single operand, with the second operand always being stored in the ax register (or the dx:ax register)
the div instruction performs integer division, the result will be always an integer
  dividing 7 by 4 gives ? result
  dividing 7 by 8 gives ? result

## Slide 17: Arithmetic Instructions - div example
Divide 1235 by 10:
mov ax, 1235
mov cl, 10
div cl
; divide ax by 10, al now contains 123 and ah contains 5
the div instruction takes a single operand, with the second operand always being stored in the ax register (or the dx:ax register)
the div instruction performs integer division, the result will be always an integer
  dividing 7 by 4 gives the result 1 with remainder 3
  dividing 7 by 8 gives the result 0 with remainder 7

## Slide 18: Input and Output (I/O)
Each microprocessor provides instructions for I/O with the devices that are attached to it (e.g., keyboard, screen)
In 8086, we use a software interrupt mechanism
The 8086 int instruction generates a software interrupt
Each I/O operation is identified by a unique number
E.g., the sub-program to display a character is sub-program number 2h. This number must be stored in the ah register

## Slide 19: Character output
Display the character ‘a’ on the screen:
mov dl, ‘a’
mov ah, 2h ;character output function
int 21h ;display character in dl

## Slide 20: Character Input
Read a character from the keyboard
mov ah, 1h ;keyboard input sub-program
int 21h ;call ms-dos to do character
; input operation, character
; entered is stored in al
mov c, al ; copy character from al to variable c
ax register is used for two purposes:
  ah specifies the sub-program number
  al stores this character

## Slide 21: A complete program to display ‘a’ on the screen
  ; file.asm: display ‘a’ on the screen
  ; author: xxx
  ; date: 14th Jan 2014
    .model small
    .stack 100h
    .code
start:
mov dl, ‘a’
mov ah, 2h ;character output function
int 21h ;display character in dl
mov ax, 4c00h ;return to DOS
int 21h
end start

## Slide 22: Example: display ‘a’ on the screen
the first 3 lines are comments to explain the purpose of the file, the author and date
.model and .stack: how your program will be stored in memory and how large a stack it requires
.code indicates where the program instructions begin
.data indicates where memory variables are defined
start indicate where your program starts
end indicate where your program finishes

## Slide 23: Control flow: jump instructions
The status register records the result of arithmetic instructions
the result can be tested by conditional jump instructions (je, ja, jne)

## Slide 24: Example
ax =2;
if (( ax – bx) != 0){
ax = ax + 1;
}
bx = bx + 1;
8086 version using jz instruction:
mov ax, 2
sub ax, bx ;ax = 2-bx
jz next1 ;jump if (ax-bx)==0
inc ax
next1:
inc bx

## Slide 25
8086 version using jz instruction:
mov ax, 2
cmp ax, bx
;set flags according to (ax-bx)
jz equals ;jumps if (ax==bx)
inc ax
equals:
inc bx
k

## Slide 26: if-then control statement
C version:
if (i==10){
i = i + 5;
j = j + 5;
}
8086 version 1 (test if i == 10 is true):
cmp i, 10
je label1
jmp rest
label1: add i, 5
add j, 5
rest:

## Slide 27
8086 version 2 (test if i != 10 is true):
cmp i, 10
jne rest
add i, 5
add j, 5
rest:
The second method only requires a single branch instruction
Implement an if-then statement in assembly language, we test the inverse of the condition used in the high-level language form of the construct