## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Assembly Language
8086 Instruction Set
Part 2

## Slide 2: Bit Manipulation
set bits (give them a value of 1)
clear bits (give them a value of 0)
complement bits (change 1 to 0, or 0 to 1)
manipulating bits is to make programs more efficient
  the program is smaller in size, required less RAM, or
  the program runs faster
  reduce the storage by using individuals bits
Logical instructions: and, or, xor, not, test

## Slide 3: clearing bits: and instruction
to clear bit 5 of a byte, we and the byte with 1101 1111
mov al, 62h ;al = 0110 0010
and al, 0dfh ;and it with 1101 1111
;al is 42h, 0100 0010
the value in the source operand, 0dfh in the example, is called a bit mask

## Slide 4: clearing bits: and instruction
in general, to clear a bit or group of bits, you define a mask consisting of 0s for the bits to be cleared and 1s everywhere else.
The bits cleared in this fashion are said to be masked out

## Slide 5: clearing bits: and instruction
In the ASCII codes of the lower-case letters, bit 5 is always 1. The corresponding upper-case letters are identical except that bit 5 is always 0.
To convert a lower-case letter to upper case, we clear bit 5 (set bit 5 to 0)
Exercise:
  The letter ‘b’ has ASCII code 62h, we convert it to ‘B’

## Slide 6: clearing bits: and instruction
answer
mov al, ‘b’ ;al=‘b’=62h 0110 0010
and al, 0dfh ;mask= 1101 1111
;al now = ‘B’ (=42h)0100 0010

## Slide 7: clearing bits: and instruction
the bit mask 1101 1111 when used with and will always set bit 5 to 0 leaving the remaining bits unchanged
xxxx xxxx ;destination bits
and 1101 1111 ;and with mask bits
xx0x xxxx ;result is that bit 5 is cleared

## Slide 8: setting bits: or instruction
the or instruction can be used to set bits to 1 regardless of their current setting
the bits set using the or instruction are said to be masked in

## Slide 9: setting bits: or instruction example
To convert a digit to its equivalent character, we need to set bits 4 and 5
the bit mask 0011 0000
e.g., convert number 7 to ASCII code for 7, that is ‘7’
mov al, 7 ;7 is 0000 0111
or al, 0011 0000b ;or with 0011 0000
;’7’ is 0011 0111

## Slide 10: setting bits: or instruction example
To convert a digit to its equivalent character, we need to set bits 4 and 5
the bit mask 0011 0000
e.g., convert number 7 to ASCII code for 7, that is ‘7’
mov al, 7 ;7 is 0000 0111
or al, 0011 0000b ;or with 0011 0000
;’7’ is 0011 0111

## Slide 11: setting bits: or instruction example
convert an upper-case letter, stored in al to its lower-case equivalent
Answer?

## Slide 12
Answer: if we have ‘A’ in al then it can be converted to ‘a’ as follows:
mov al, ‘A’ ;al=‘A’= 0100 0001
or al, 20h ;or with 0010 0000
;gives al=‘a’ 0110 0001

## Slide 13: xor instruction
the xor instruction can be used to toggle the value of specific bits
the bit mask to toggle particular bits should have 1’s for any bit position you wish to toggle and 0’s for bits which are to remain changed
E.g., toggle bits 0, 1, and 6 of the value in al (here 67h)
mov al, 67h ;al= 0011 0111
xor al, 08h ;xor it with 0100 0011
;al is 34h 0111 0100

## Slide 14: xor instruction
the xor instruction can be used to toggle the value of specific bits
the bit mask to toggle particular bits should have 1’s for any bit position you wish to toggle and 0’s for bits which are to remain changed
E.g., toggle bits 0, 1, and 6 of the value in al (here 67h)
mov al, 67h ;al= 0011 0111
xor al, 08h ;xor it with 0100 0011
;al is 34h 0111 0100

## Slide 15: xor instruction
a common use of xor is to clear a register (set all bits to 0).
xor cx, cx
use mov instruction to clear a register
mov cx, 0
  but slower to execute and occupies more memory than the xor instruction
sub instruction can use to clear a register
sub cx, cx

## Slide 16: not instruction
not instruction inverts all of its bits of its operand
mov al, 33h ;al = 0011 0011
not al ;al= 1100 1100

## Slide 17: Efficiency
the xor instruction is used to clear an operand
the or/and instructions may be used to compare an operand to 0
comparing an operand to 0 using logical instructions
or cx, cx ;compares cx with 0
je label
and ax, ax ;compares ax with 0
jg label2
comparing an operand to 0 using cmp instructions:
cmp cx, 0
je label
cmp ax, 0
jg label12

## Slide 18: test instruction
To determine if a particular bit is set to a 1 or 0, we can use and instruction, and a mask which clears the remaining bits (a mask with the bit to be tested set to 1)
e.g., we test if bit 1 of al is 1 or 0, we use a mask with bit 1 set, the mask: 0000 0010
and al, 0000 0010b ;mask has bit 1 set
jz bit1_clear ;go to bit1_clear if bit1==0

## Slide 19: test instruction
the and instruction will clear all bits in al except bit 1
the disadvantage of testing a bit using and instruction is that the content of al are destroyed (akin to the use of sub ax, ax to compare with ax with 0)
the test instruction operates exactly like the and instruction, except that the contents of the destination register are not modified (akin to using cmp ax, 0)

## Slide 20: test instruction examples
Test if bit 1 of al is clear using the test instruction
test al, 0000 0010b
jz bit1_clear
Test if any bits of 0,1,6 or 7 are set:
test al, 1100 0011b
jnz bit_set

## Slide 21: Shifting and rotating bits
Bits can be moved right or left
Values shifted off the end of an operand are lost (one may go into the carry flag)
Shift instruction moves bits a specified number of places to the right or left
Rotate instruction moves bits a specified number of places to the right or left. For each bit rotated, the last bit in the direction of the rotate is moved into the first bit position at the other end of the operand

## Slide 22: Shifting and rotating bits
Shift instructions are often used to carry out multiplication and division.
  e.g., multiple a number by 10 in decimal, simply shift the number left one digit and add a 0 on the right hand side
  e.g., division by 10 shifts the decimal point in the opposite direction
The number 0000 0100 (4) when shifted left one bit, gives 0000 1000 (8), so shift left one bit is equivalent to multiplying by 2. Shifting left by 2 bits effectively multiplies by 4 (22)
shifting left n bits multiplies by 2n.
sh1 (shift left): shift bits to left
shr (shift rigt): shift bits to right
sar (shift arithmetic left), which causes the sign bit to be shifted into itself

## Slide 23: Shifting and rotating bits
In the case of division, a right shift of n bits divides by a number of 2n,
use the sar (shift arithmetic right) instruction if we wish to preserve the sign bit
e.g., dividing al (which contains 12) by 2 using sar instruction
mov al, 12 ;al = 0000 1100
sar a1, 1 ;divide by 2
;al now contains 6

## Slide 24: Shifting and rotating bits
here we see the difference between the sar and shr instructions:
mov al, 0a0h ;al=-96d=1010 0000 in 2’s complement
mov cl, 3 ;divide by 8
sar al, cl ;al=—12d=1111 0100 in 2’s complement
mov al, 0a0h ;al=160d=1010 0000 as unsigned number
mov cl, 3 ;divide by 8
shr al, cl ;al=20d=0001 0100 in 2’s complement

## Slide 25: sar instruction
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
7
0
al before
sar al, cl
1 | 1 | 1 | 1 | 0 | 1 | 0 | 0
7
0
al after
sar al, cl
0
00
carry flag

## Slide 26: shr instruction
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0
7
0
al before
shr al, cl
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
7
0
al after
shr al, cl
0
00
carry flag

## Slide 27: Rotate instruction
rotate the bits in an operand
if we rotate the al register by 2 bits, then bit 7 rotates to position 1; bit 6 rotates to position 0
ror (rotate right)
rol (rotate left)

## Slide 28: Rotate instruction - example
if al contains 0110 0011, then after rotating by one bit to the right al will contain 1011 0001. If we then rotate al two bits to the left al will contain 1100 0110
mov al, 47h ;al = 0110 0011
ror al, 1 ;al now contains 1011 0001
mov cl, 2 ;cl=2
rol al, cl ;al now contains 1100 0110

## Slide 29: Rotate instruction - example
Use the ror instruction to swap the high-order bits with low-order bits of bl. The register bl contains 0110 0111
answer?

## Slide 30: Rotate instruction - example
Use the ror instruction to swap the high-order bits with low-order bits of bl. The register bl contains 0110 0111
answer:
mov bl, 0110 0111b ;b1= 0110 0111
mov cl, 4
ror bl, cl ;b1 now contains 0111 0110

## Slide 31: Questions
What is difference between register and memory? What are there specific uses?

## Slide 32: Register vs. Memory
Registers are temporary storage in the CPU that holds the data the processor is currently working on, while memory holds the program instructions and the data the program requires.
Data has to be loaded into a CPU register from memory before the CPU can process it. Memory is much slower than registers, the fastest operations work directly with registers.
There is a lot more memory than registers, there are generally only a few registers available on a processer, e.g., stack register, flags register, program counter, and some addressing registers.