## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Assembly Language
8086 Instruction Set

## Slide 2
Parameters Passing

## Slide 3: Sub-program parameter passing
First method to pass parameter to sub-programs:
  To place the parameters in registers. E.g., I/O sub-program use the ax register to act as a parameter
  But we only have 2 or 3 registers available for parameter passing purposes

## Slide 4: Sub-program parameter passing
Second method is to pass the address of a list of parameters to the sub-programs
The parameter list may be of arbitrary length, so long as the list is stored contiguously in memory
We use the ax register to store the address of the list to be passed; use bx to access the element of the list

## Slide 5: Sub-program parameter passing - example
Defining and using the sum sub-program, which access a list of four parameters passed via the bx register

## Slide 6
;sum.asm: sums 4 numbers
.model small
.stack 100h
.data
arg1 dw 3 ;these 4 variable form a list
arg2 dw 7 ;since they are defined together
arg3 dw 4
arg4 dw 11
.code
start:
mov ax, @data
mov ds, ax
mov bx, offset arg1 ;bx=address of list
call sum ;compute sum and store it in ax
call putn ;display result
mov ax, 4c00h
int 21h

## Slide 7
sum:
;returns sum of 4 element list in ax
mov ax, [bx] ;ax = arg1
add bx, 2 ;bx points to arg2
add ax, [bx] ;ax = ax + arg2
add bx, 2 ;bx points to arg3
add ax, [bx] ;ax = ax + arg3
add bx, 2 ;bx points to arg4
add ax, [bx] ;ax = ax + arg4
ret
… ;insert code here for putn etc
end start
Why 2?

## Slide 8
sum:
;returns sum of 4 element list in ax
mov ax, [bx] ;ax = arg1
add bx, 2 ;bx points to arg2
add ax, [bx] ;ax = ax + arg2
add bx, 2 ;bx points to arg3
add ax, [bx] ;ax = ax + arg3
add bx, 2 ;bx points to arg4
add ax, [bx] ;ax = ax + arg4
ret
… ;inset code here for putn etc
end start
bx register increased by 2 to point to successive elements in the list (the elements are word sized (16 bits))

## Slide 9
The above code can be more efficient, we write [bx+2], [bx+4], [bx+6] to specify the addresses of the parameters, i.e., we can use base addressing to access the parameters
sum: ;return the sum of 4 elements
mov ax, [bx] ;ax = arg1
add ax, [bx+2] ;ax = ax + arg2
add ax, [bx+4] ;ax = ax + arg3
add ax, [bx+6] ;ax = ax + arg4
ret

## Slide 10: Sub-program parameter passing – stack
Use stack to pass parameters
As many parameters as desired may be pushed on the stack before the sub-program is called. The sub-program can then access them on the stack
Potential problem: the call instruction pushes the return address on the stack. If the sub-program were to simply pop the stack to obtain a parameter, it would first pop off the return address. This would have to be saved and pushed back on the stack in order for the ret instruction to work

## Slide 11: Sub-program parameter passing – stack
push arg4
push arg3
push arg2
push arg1
call sum
We must first push the parameters on to the stack
The bp register, like the sp register, always references the stack segment
...
…
Return address
Parameter 1
Parameter 2
Parameter 3
Parameter 4
Stack
bp
sp
Low address
High address
After executing
mov bp, sp

## Slide 12: Sub-program parameter passing – stack
We need to access the stack without changing sp
Copy the value of sp into bp (mov bp, sp)
[bp] refers to the value on the stack pointed by bp
sum:
mov bp, sp
mov ax, [bp+2]
add ax, [bp+4]
add ax, [bp+6]
add ax, [bp+8]
ret

## Slide 13: Sub-program parameter passing – stack
We have not modified sp, the ret instruction to return appropriately.
Always clear items from the stack when we have finished using them

## Slide 14: Sub-program parameter passing – stack
Three possible solutions to clear the stack:
Uses a pop for each value pushed on:
Modify sp directly, by adding 2 for each push instruction, after calling the sub-program. Four items were pushed on the stack, so add 8 to the sp register to clear the stack:
call sum
add sp, 8
8086 provides for an operand to be included with the ret instruction. The sub-program can be terminated with:
ret 8
This ret instruction will add 8 to sp after obtaining the return address

## Slide 15: Sub-program parameter passing – stack
Rewrite sum as follows:
sum:
mov bp, sp
mov ax, [bp+2]
add ax, [bp+4]
add ax, [bp+6]
add ax, [bp+8]
ret 8

## Slide 16: Macros
CR equ 13
The assembler replaces all occurrences of CR with the number 13 before the program is translated to machine code.
i.e., the equ directive provides a text substitution facility. Such a facility is called a macro facility
Define a macro:
sample macro [parameter-list]
;text (body) of macro may be done one
; or many lines
endm

## Slide 17: Macros - example
Define macros to swap the contents of ax with bx and to add the registers ax, bx, cx, and dx, leaving the sum in ax:
swap marco
mov cx, bx
mov bx, ax
mov ax, cx
endm
add_regs macro
add ax, bx
add ax, cx
add ax, dx
endm
marco can be defined anywhere in your program, but must be defined before they are first called

## Slide 18: Macros - example
using the swap and add_regs marcos:
mov ax, 10
mov bx, 20
swap
mov cx, 4
mov dx, 6
add_regs
NOTE: The 8086 provides the xchg instruction to swap the contents of two registers with a memory variable, e.g.,
xchg ax, bx ;swap ax with bx
xchg dx, y ;swap dx and memory variable y

## Slide 19: Macros vs. Sub-programs
for sub-program, the call instruction transfers control to the sub-program and the ret instruction transfer control from the sub-program at run-time
A macro results in the assembler expanding the name of the macro into the defined set of instructions and inserting them at that point in the program, just as if you entered them there.
  There is no transfer of control involved in the use of macro
  provides a text substitution facility

## Slide 20: Macros vs. Sub-programs
Advantage of macros:
  We use sub-programs, the return address has to be pushed on the stack by the call instruction and retrieved from there by the ret instruction. This represents an overhead in the time taken to carry out these operations
  If time is critical in an application, this overhead can be reduced by not using sub-programs
  By defining this code in the form of a macro, we can make programs easier to read without sacrificing speed of execution

## Slide 21: Macros with parameters
We could write a macro add_regs which sums any 3 registers that are passed as parameters. The result is stored in the first parameters.
add_regs macros r1, r2, r3
add r1, r2
add r1, r3
endm
We can use add_regs to sum any 3 registers:
add_regs ax, bx, cx
add_regs cx, dx, si
The assembler will replace r1, r2, r3, which are called dummy parameters, by the values specified in the macro call, which are referred to as actual parameters