## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Prof. Peter Edwards
p.edwards@abdn.ac.uk

## Slide 2: Course Outline
Basics: Number Systems, (Decimal Binary Hexadecimal), Binary Addition, Logic Gates, Transistors, Power Consumption, Boolean Algebra, Multiplexer/Decoders/Timing, Latches and Flip-Flops, Finite State Machines.
Building Blocks: Arithmetic Circuits, Number Systems (Fixed-Point, Floating-Point), Memory Arrays, Logic Arrays.
Assembly Language, Machine Language, Addressing Modes, Program execution, Heaps and stacks.
Microarchitecture: Single-Cycle Processor, Multicycle Processor, Pipelined Processor.
Memory Systems: Caches, Virtual Memory.

## Slide 3: Principles of Computer Architecture

## Slide 4: How to Manage Complexity
Abstraction
Discipline
The Three –Y’s
  Hierarchy
  Modularity
  Regularity

## Slide 5: Abstraction
Level of abstraction for an electronic computing system
Hiding details when they aren’t important

## Slide 6: Discipline …
Intentionally restrict design choices so that you can work more productively at a higher level of abstraction.
Using interchangeable parts is a familiar application of discipline.
Digital discipline: digital circuits use discrete voltages
  Discrete voltages instead of continuous voltages
  Simpler to design than analog circuits – can build more sophisticated systems
  Digital systems replacing analog predecessors:
    i.e., digital cameras, digital television, dvds …
Notes: Interchangeable parts – think about mass-production manufacturing – cars, washing machines – not possible without interchangeable parts.

## Slide 7: The 3 Y’s
Hierarchy
  A system divided into modules and submodules.
Modularity
  Having well-defined functions and interfaces.
Regularity
  Encouraging uniformity, so modules can be easily reused.

## Slide 8: Being Digital …

## Slide 9: Digital Abstraction
Most physical variables are continuous
  Voltage on a wire
  Frequency of an oscillation
Digital systems are concerned with digital signals
Digital signals can take many forms
Here we will concentrate on binary signals since these are the most common form of digital signals:
  can be used individually
    perhaps to represent a single binary quantity or the state of a single switch
  can be used in combination
    to represent more complex quantities

## Slide 10: Binary Quantities & Variables
A binary quantity is one that can take only 2 states
A simple binary arrangement
S | L
OPEN | OFF
CLOSED | ON
S | L
0 | 0
1 | 1
A truth table

## Slide 11: Digital Discipline: Binary Matters
Two discrete values:
  1’s and 0’s
  1, TRUE, HIGH
  0, FALSE, LOW
1 and 0: voltage levels, rotating gears, fluid levels, etc.
Digital circuits use voltage levels to represent 1 and 0
Bit: Binary digit

## Slide 12: Number Systems

## Slide 13: Two Common Number Systems
Decimal
Binary

## Slide 14: Powers of Two – 2n
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768
Notes: Handy to memorize up to 210
1024 bytes (210 bytes) – traditionally 1KB
Mega (M) = 220
Giga (G) = 230
Tera (T) = 240

## Slide 15: Number Conversion
Binary to decimal conversion:
  Add up decimal equivalent of individual values.
Decimal to binary conversion:
  Repeatedly divide by the base and remember the remainder.
  Convert 100112 to decimal
  100112 = (1 x 24) + (0 x 23) + (0 x 22) + (1 x 21) + (1 x 20)
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
  Convert 4710 to binary
  Start: 47 -
  /2 23 1
  /2 11 1
  /2 5 1
  /2 2 1
  /2 1 0
  /2 0 1
  Read number
  from bottom =
  1011112

## Slide 16: Binary Values & Range
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]
Notes: What is the value of 224?
24 × 220 ≈ 16 million
How many values can a 32-bit variable represent?
22 × 230 ≈ 4 billion

## Slide 17: Hexadecimal Numbers (Base 16)
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111
e.g. 4AFh
0x4AF
Notes: Hex codes are used as a useful shorthand for binary. It is important to note that computers do not use hexadecimal - it is used by humans to shorten binary to a more easily understandable form. Hexadecimal is translated into binary for computer use. Some examples of where hex is used include:
colour references
assembly language programs
error messages
0x preface indicates hexadecimal; this originated with the C programming language – to help compiler that what came next was Hexadecimal constant.
eg. 0x4AF
Hex can be used to represent colours on web pages and image-editing programs using the format #RRGGBB (RR = reds, GG = greens, BB = blues). The # symbol indicates that the number has been written in hex format.
This system uses two hex digits for each colour, eg #FF6600.
As one hex digit represents 4 bits, two hex digits together make 8 bits (1 byte). The values for each colour run between 00 and FF.
In binary, 00 is 0000 0000 and FF is 1111 1111. That provides 256 possible values for each of the three colours.
That gives a total spectrum of 256 reds x 256 greens x 256 blues - which is over 16 million colours in total.
#FF0000 will be the purest red - red only, no green or blue.
Black is #000000 - no red, no green and no blue.
White is #FFFFFF.

## Slide 18: Hexadecimal to Binary Conversion
Hexadecimal to binary conversion:
  Each hex symbol corresponds to 4 bits.
Hexadecimal to decimal conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  4: 0100
  A: 1010
  F: 1111
  0100 1010 11112
  Convert 4AF16 to decimal
  4AF16 = (4 x 162) + (10 x 161) + (15 x 160)
  (4 x 256) + (10 x 16) + (15 x 1)
  119910

## Slide 19: Bits, Bytes & Nibbles
Bits
Bytes & Nibbles
Bytes

## Slide 20: Numeric & Alphabetic Codes
ASCII code
  American Standard Code for Information Interchange
  Each character represented by a 7-bit code
    gives 128 possible characters
    codes defined for upper and lower-case alphabetic characters, digits 0 – 9, punctuation marks and various non-printing control characters (such as return and backspace)
Notes: ASCII was the most common character encoding on the World Wide Web until December 2007, when it was surpassed by UTF-8, which includes ASCII as a subset.
UTF-8:
The first 128 characters (US-ASCII) need one byte. The next 1,920 characters need two bytes to encode. This covers the remainder of almost all Latin alphabets, and also Greek, Cyrillic, Coptic, Armenian, Hebrew, Arabic, Syriac and Tāna alphabets.

## Slide 21: Binary Addition
Add the following 4-bit binary numbers:
Add the following 4-bit binary numbers:
OVERFLOW!
Notes: Rules for binary addition:
0 + 0 = 0 carry 0
0 + 1 = 1 carry 0
1 + 0 = 1 carry 0
1 + 1 = 0 carry 1

## Slide 22: Overflow
Digital systems operate on a
fixed number of bits
Overflow
  When result is too big to fit in the available number of bits.
See previous example of 1011 + 0110
Notes: A microprocessor or computing system usually uses FIXED PRECISION for integers; they limit the numbers to a fixed number of bits
Overflow occurs when two numbers are added or subtracted , and the correct result is a number that is outside of the range of allowable numbers for that precision.

## Slide 23: Signed Integers
The problem with signed integers ( - 45, + 27, -99) is the sign. How do we encode the sign?
The sign is an extra piece of information that has to be encoded in addition to the magnitude.
Signed Magnitude (SM) is a method for encoding signed integers.
The Most Significant Bit is used to represent the sign. ‘1’ is used for a ‘-’ (negative sign), a ‘0’ for a ‘+’ (positive sign).
The format of a SM number in 8 bits is: s n n n n n n n
sign bit

## Slide 24: Signed Magnitude
For 8 bits, can represent the signed integers:
127 to +127
For N bits, can represent the signed integers:
-(2(N-1) – 1) to +( 2(N-1) – 1)
-5 = 1 0000101 +5 = 0 0000101
BUT What about zero? 1 0000000 or 0 0000000 ?
What about addition?
1 0000101 -5
+ 0 0000101 +5
1 0001010 ??
Notes: Signed magnitude easy to understand and encode (similar to that which people commonly use).
One problem is that it has two ways of representing 0 (-0, and +0) . Mathematically speaking, no such thing as two representations for zeros.
Another problem is that addition of K + (-K) does not give Zero (if the numbers are operated on directly with the sign bit in place). -5 + 5 = -10

## Slide 25: Next …
One & Two’s Complement