## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 6
David Money Harris and Sarah L. Harris

## Slide 2
Architecture: programmer’s view of computer
  Defined by instructions & operand locations
Microarchitecture: how to implement an architecture in hardware (covered in Chapter 7)
Introduction

## Slide 3
Instructions: commands in a computer’s language
  Assembly language: human-readable format of instructions
  Machine language: computer-readable format (1’s and 0’s)
MIPS architecture:
  Developed by John Hennessy and his colleagues at Stanford and in the 1980’s.
  Used in many commercial systems, including Silicon Graphics, Nintendo, and Cisco
Once you’ve learned one architecture, it’s easy to learn others
Assembly Language

## Slide 4
Underlying design principles, as articulated by Hennessy and Patterson:
    Simplicity favors regularity
    Make the common case fast
    Smaller is faster
    Good design demands good compromises
Architecture Design Principles

## Slide 5
add: mnemonic indicates operation to perform
b, c: source operands (on which the operation is performed)
a: destination operand (to which the result is written)
C Code
a = b + c;
MIPS assembly code
add a, b, c
Instructions: Addition

## Slide 6
Similar to addition - only mnemonic changes
sub: mnemonic
b, c: source operands
a: destination operand
C Code
a = b - c;
MIPS assembly code
sub a, b, c
Instructions: Subtraction

## Slide 7
Simplicity favors regularity
Consistent instruction format
Same number of operands (two sources and one destination)
easier to encode and handle in hardware
Design Principle 1

## Slide 8
More complex code is handled by multiple MIPS instructions.
C Code
a = b + c - d;
MIPS assembly code
add t, b, c # t = b + c
sub a, t, d # a = t - d
Multiple Instructions

## Slide 9
Make the common case fast
MIPS includes only simple, commonly used instructions
Hardware to decode and execute instructions can be simple, small, and fast
More complex instructions (that are less common) performed using multiple simple instructions
MIPS is a reduced instruction set computer (RISC), with a small number of simple instructions
Other architectures, such as Intel’s x86, are complex instruction set computers (CISC)
Design Principle 2

## Slide 10
An instruction operates on operands.
  Operands can be stored in registers or memory, or may be constants (also called immediates) stored in the instruction itself.
Operands

## Slide 11
MIPS has 32 32-bit registers
Registers are faster than memory
MIPS called “32-bit architecture” because it operates on 32-bit data
Operands: Registers

## Slide 12
Smaller is Faster
MIPS includes only a small number of registers
Design Principle 3

## Slide 13
Name | Register Number | Usage
$0 | 0 | the constant value 0
$at | 1 | assembler temporary
$v0-$v1 | 2-3 | Function return values
$a0-$a3 | 4-7 | Function arguments
$t0-$t7 | 8-15 | temporaries
$s0-$s7 | 16-23 | saved variables
$t8-$t9 | 24-25 | more temporaries
$k0-$k1 | 26-27 | OS temporaries
$gp | 28 | global pointer
$sp | 29 | stack pointer
$fp | 30 | frame pointer
$ra | 31 | Function return address
MIPS Register Set

## Slide 14
Registers:
  $ before name
  Example: $0, “register zero”, “dollar zero”
Registers used for specific purposes:
    $0 always holds the constant value 0.
    the saved registers, $s0-$s7, used to hold variables
    the temporary registers, $t0 - $t9, used to hold intermediate values during a larger computation
    Discuss others later
Operands: Registers

## Slide 15
Revisit add instruction
C Code
a = b + c
MIPS assembly code
# $s0 = a, $s1 = b, $s2 = c
add $s0, $s1, $s2
Instructions with Registers

## Slide 16
Too much data to fit in only 32 registers
Store more data in memory
Memory is large, but slow
Commonly used variables kept in registers
Operands: Memory

## Slide 17
Each 32-bit data word has a unique address
Word-Addressable Memory

## Slide 18
Memory read called load
Mnemonic: load word (lw)
Format:
lw $s0, 5($t1)
Address calculation:
  add base address ($t1) to the offset (5)
  Effective address = ($t1 + 5)
Result:
  $s0 holds the value at address ($t1 + 5)
Any register may be used as base address
Reading Word-Addressable Memory

## Slide 19
Example: read a word of data at memory address 1 into $s3
  address = ($0 + 1) = 1
  $s3 = 0xF2F1AC07 after load
Assembly code
lw $s3, 1($0) # read memory word 1 into $s3
Reading Word-Addressable Memory
Hexadecimal constants are written with the prefix 0x.
By contention, memory is drawn with low memory addresses toward the bottom and high memory addresses towards the top

## Slide 20
Memory write are called store
Mnemonic: store word (sw)
Writing Word-Addressable Memory

## Slide 21
Example: Write (store) the value in $t4 into memory address 7
  add the base address ($0) to the offset (0x7)
  address: ($0 + 0x7) = 7
  Offset can be written in decimal (default) or hexadecimal
Assembly code
sw $t4, 0x7($0) # write the value in $t4
# to memory word 7
Writing Word-Addressable Memory

## Slide 22
Each data byte has unique address
Load/store words or single bytes: load byte (lb) and store byte (sb)
32-bit word = 4 bytes, so word address increments by 4
Byte-Addressable Memory

## Slide 23
The address of a memory word must now be multiplied by 4. For example,
  the address of memory word 2 is 2 × 4 = 8
  the address of memory word 10 is 10 × 4 = 40 (0x28)
MIPS is byte-addressed, not word-addressed
Reading Byte-Addressable Memory

## Slide 24
Example: Load a word of data at memory address 4 into $s3.
$s3 holds the value 0xF2F1AC07 after load
MIPS assembly code
lw $s3, 4($0) # read word at address 4 into $s3
Reading Byte-Addressable Memory

## Slide 25
Example: stores the value held in $t7 into memory address 0x2C (44)
MIPS assembly code
sw $t7, 44($0) # write $t7 into address 44
Writing Byte-Addressable Memory

## Slide 26
Good design demands good compromises
Multiple instruction formats allow flexibility
  add, sub: use 3 register operands
  lw, sw: use 2 register operands and a constant
Number of instruction formats kept small
  to adhere to design principles 1 and 3 (simplicity favors regularity and smaller is faster).
Design Principle 4

## Slide 27
lw and sw use constants or immediates
immediately available from instruction
16-bit two’s complement number
addi: add immediate
Subtract immediate (subi) necessary?
C Code
a = a + 4;
b = a – 12;
MIPS assembly code
# $s0 = a, $s1 = b
addi $s0, $s0, 4
addi $s1, $s0, -12
Operands: Constants/Immediates

## Slide 28
Binary representation of instructions
Computers only understand 1’s and 0’s
32-bit instructions
  Simplicity favors regularity: 32-bit data & instructions
3 instruction formats:
  R-Type: register operands
  I-Type: immediate operand
  J-Type: for jumping (discuss later)
Machine Language

## Slide 29
Register-type
3 register operands:
  rs, rt: source registers
  rd: destination register
Other fields:
  op: the operation code or opcode (0 for R-type instructions)
  funct: the function
  with opcode, tells computer what operation to perform
  shamt: the shift amount for shift instructions, otherwise it’s 0
R-Type

## Slide 30
Note the order of registers in the assembly code:
add rd, rs, rt
R-Type Examples

## Slide 31
Immediate-type
3 operands:
  rs, rt: register operands
  imm: 16-bit two’s complement immediate
Other fields:
  op: the opcode
  Simplicity favors regularity: all instructions have opcode
  Operation is completely determined by opcode
I-Type

## Slide 32
Note the differing order of registers in assembly and machine codes:
addi rt, rs, imm
lw rt, imm(rs)
sw rt, imm(rs)
I-Type Examples

## Slide 33
Jump-type
26-bit address operand (addr)
Used for jump instructions (j)
Machine Language: J-Type

## Slide 34
Review: Instruction Formats

## Slide 35
32-bit instructions & data stored in memory
The stored program offers general purpose computing
To run a new program:
  No rewiring required
  Simply store new program in memory
Program Execution:
  Processor fetches (reads) instructions from memory in sequence
  Processor performs the specified operation
The architectural state of a microprocessor holds the state of a program. For MIPS, it consists of the register file and a program counter (PC)
Power of the Stored Program

## Slide 36
The Stored Program
Program Counter (PC): keeps track of current instruction

## Slide 37
Start with opcode: tells how to parse rest
If opcode all 0’s
  R-type instruction
  Function bits tell operation
Otherwise
  opcode tells operation
Interpreting Machine Code

## Slide 38
High-level languages:
  e.g., C, Java, Python
  Written at higher level of abstraction
Common high-level software constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming

## Slide 39
and, or, xor, nor
  and: useful for masking bits
    Masking all but the least significant byte of a value:
    0xF234012F AND 0x000000FF = 0x0000002F
  or: useful for combining bit fields
    Combine 0xF2340000 with 0x000012BC:
    0xF2340000 OR 0x000012BC = 0xF23412BC
  nor: useful for inverting bits:
    A NOR $0 = NOT A
andi, ori, xori
  16-bit immediate is zero-extended (not sign-extended)
  nori not needed
Logical Instructions

## Slide 40
Logical Instructions Example 1

## Slide 41
Logical Instructions Example 1

## Slide 42
Logical Instructions Example 2

## Slide 43
Logical Instructions Example 2

## Slide 44
sll: shift left logical
  Example: sll $t0, $t1, 5 # $t0 <= $t1 << 5
srl: shift right logical
  Example: srl $t0, $t1, 5 # $t0 <= $t1 >> 5
sra: shift right arithmetic
  Example: sra $t0, $t1, 5 # $t0 <= $t1 >>> 5
Shift Instructions

## Slide 45
Shift Instructions

## Slide 46
Shift Instructions

## Slide 47
Execute instructions out of sequence
Types of branches:
  Conditional
    branch if equal (beq)
    branch if not equal (bne)
  Unconditional
    jump (j)
    jump register (jr)
    jump and link (jal)
Branching

## Slide 48
Review: The Stored Program

## Slide 49
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
beq $s0, $s1, target # branch is taken
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target: # label
add $s1, $s1, $s0 # $s1 = 4 + 4 = 8
Labels indicate instruction location. They can’t be reserved words and must be followed by colon (:)
Conditional Branching (beq)

## Slide 50
# MIPS assembly
addi $s0, $0, 4 # $s0 = 0 + 4 = 4
addi $s1, $0, 1 # $s1 = 0 + 1 = 1
sll $s1, $s1, 2 # $s1 = 1 << 2 = 4
bne $s0, $s1, target # branch not taken
addi $s1, $s1, 1 # $s1 = 4 + 1 = 5
sub $s1, $s1, $s0 # $s1 = 5 – 4 = 1
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5
The Branch Not Taken (bne)

## Slide 51
# MIPS assembly
addi $s0, $0, 4 # $s0 = 4
addi $s1, $0, 1 # $s1 = 1
j target # jump to target
sra $s1, $s1, 2 # not executed
addi $s1, $s1, 1 # not executed
sub $s1, $s1, $s0 # not executed
target:
add $s1, $s1, $s0 # $s1 = 1 + 4 = 5
Unconditional Branching (j)

## Slide 52
# MIPS assembly
addi $s0, $0, 0x2010
jr $s0
addi $s1, $0, 1
sra $s1, $s1, 2
lw $s3, 44($s1)
jr is an R-type instruction.
jr jumps to the address held in a register
Unconditional Branching (jr)