## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 7
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 7 :: Topics
Introduction
Performance Analysis
Single-Cycle Processor
Multicycle Processor
Pipelined Processor

## Slide 3
Microarchitecture: the specific arrangement of registers, ALUs, finite state machines (FSMs), memories, and other logic building blocks needed to implement an architecture.
Introduction

## Slide 4
Design Process:
  Datapath: operates on words of data. It contains structures such as memories, registers, ALUs, and multiplexers
  Control: receives the current instruction from the datapath and tells the datapath how to execute that instruction. It produces multiplexer select, register enable, and memory write signals to control the operation of the datapath
Introduction

## Slide 5
Multiple implementations for a single architecture:
  Single-cycle: Each instruction executes in a single cycle
  Multicycle: Each instruction is broken into series of shorter steps
  Pipelined: Each instruction broken up into series of steps & multiple instructions execute at once
Microarchitecture

## Slide 6
Program execution time
Execution Time = (#instructions)(cycles/instruction) (seconds/cycle)
Definitions:
  CPI: The number of cycles per instruction is the number of clock cycles required to execute an average instruction
  CPI: Cycles/instruction
  IPC: instructions/cycle = IPC
  Clock period: The number of seconds per cycle is the clock period Tc
  Tc = seconds/cycle
Challenge is to satisfy constraints of:
  Cost
  Power
  Performance
Processor Performance

## Slide 7
Consider subset of MIPS instructions:
  R-type instructions: and, or, add, sub, slt
  Memory instructions: lw, sw
  Branch instructions: beq
MIPS Processor
  lw: load word, to read a data word from memory into a register, it specifies the effective address in memory as the sum of a base address and an offset.
  e.g., lw $s3, 1($0)
  The base address is $0, which holds the value 0, and the offset is 1, so the lw instruction reads from memory address ($0 + 1) = 1.
  After the lw instruction is executed, $s3 holds the data value stored at memory address 1.

## Slide 8
Consider subset of MIPS instructions:
  R-type instructions: and, or, add, sub, slt
  Memory instructions: lw, sw
  Branch instructions: beq
MIPS Processor
  beq: branch if equal, braches when the values in two registers are equal
  sw: store word, to write a data word from a register to a memory
  e.g., sw $s7, 5($0)
  writes the contents of register $7 into memory word 5

## Slide 9
Determines everything about a processor:
  Program Counter
  Instruction Memory
  Register file
  Data memory
Architectural State

## Slide 10
MIPS State Elements
Program counter: its output PC points to the current instruction; its input PC’ indicates the address of the next instruction.
Instruction Memory: takes a 32-bit instruction address input, A, and reads the 32-bit data (i.e., instruction) from that address onto the read data output, RD.

## Slide 11
MIPS State Elements
Register file: two read ports specify as source operands, they read the 32-bit register values onto read data output RD1 and RD2. The write port takes a 5-bit address input, A3; a 32-bit write data input WD. A write enable input WE3; and a clock
Data memory: if the write enable WE is 1, it writes data WD into address A on the rising edge of the clock. If the write enable WE is 0, it reads address A onto RD.

## Slide 12
Executes an entire instruction in one cycle
Datapath
Control
Single-Cycle MIPS Processor

## Slide 13
STEP 1: Fetch instruction from memory
Single-Cycle Datapath: lw fetch
PC register contains the address of the instruction to execute.
The first step is to read this instruction from instruction memory.
The instruction memory reads out, or fetches, the 32-bit instruction, labeled Instr
lw $t2, 32($0)

## Slide 14
STEP 2: Read source operands from register file
The next step is to read the source register containing the base address. This register is specified in the rs field of the instruction, Instr25:21.
Single-Cycle Datapath: lw Register Read

## Slide 15
STEP 2: Read source operands from register file
Single-Cycle Datapath: lw Register Read
I-type instructions use two register operands and one immediate operand.
The 32-bit instruction has 4 fields: op, rs, rt, imm.
rs and imm are the source registers; rt is the destination for addi and lw instructions

## Slide 16
STEP 2: Read source operands from register file
The next step is to read the source register containing the base address. This register is specified in the rs field of the instruction, Instr25:21.
Single-Cycle Datapath: lw Register Read
lw $t2, 32($0)
rs = $0

## Slide 17
STEP 3: Sign-extend the immediate
Single-Cycle Datapath: lw Immediate
The lw instruction requires an offset. The offset is stored in the immediate field of the instruction, Instr15:0.
The 16-bit immediate might be either positive or negative, it must be sign-extended to 32 bits
SignImm15:0 = Instr15:0; SignImm31:16 = Instr15
lw $t2, 32($0)
rs = $0
SignImm15:0 = 32

## Slide 18
STEP 4: Compute the memory address
Single-Cycle Datapath: lw address
lw $t2, 32($0)
rs = $0
SignImm15:0 = 32
ALUResult = 0 + 32 = 32
The process must add the base address to the offset to find the address to read from memory.
ALUControl is set to 010 to add the base address and offset
ALUResult is sent to the data memory as the address for the load instruction

## Slide 19
STEP 5: Read data from memory and write it back to register file
Single-Cycle Datapath: lw Memory Read
The data is read from the data memory onto the ReadData bus, then written back to the destination register in the register file at the end of the cycle.
The destination register for the lw instruction is specified in the rt field, Instr20:16, which is connected to the port 3 address input A3.
ReadData is connected to to WD3.
The write takes place on the rising edge of the clock

## Slide 20
STEP 5: Read data from memory and write it back to register file
Single-Cycle Datapath: lw Memory Read
lw $t2, 32($0)
rs = $0
SignImm15:0 = 32
ALUResult = 0 + 32 = 32
rt = $t2
$t2 holds the data value stored at memory address 32

## Slide 21
STEP 6: Determine address of next instruction
Single-Cycle Datapath: lw PC Increment
The process must compute the next instruction.
Instructions are 32 bits = 4 bytes, the next instruction is PC + 4.
The new address is written into the program counter on the next rising edge of the clock.

## Slide 22
sw instruction reads a second register from the register file and writes it to the data memory
The register is specified in the rt field, Instr20:16.
The register value is read onto the RD2 port
MemWrite = 1 to write the data to memory
Single-Cycle Datapath: sw

## Slide 23
ALUcontrol = 010, to add the base address and offset;
RegWrite = 0, nothing to be written to the register file
ReadData is ignored because RegWrite = 0
Single-Cycle Datapath: sw

## Slide 24
R-type: register-type
R-type instructions use three registers as operands: two as sources, one as a destination.
The 32-bit instruction has 6 fields: op, rs, rt, rd, shamt and funct.
R-type instructions: add, sub, and, or and slt
e.g., add $s0, $s1, $s2
rs = $s1, rt = $s2, rd = $s0
Single-Cycle Datapath: R-Type

## Slide 25
add rd, rs, rt
Read from rs (Instr25:21) and rt (Instr20:16)
Single-Cycle Datapath: R-Type

## Slide 26
Add a MUX to choose SrcB from either the register file RD2 port or SignImm
ALUSrc = 0 for R-type to choose SrcB from the register file; ALUSrc = 1 for lw and sw to choose SignImm
Single-Cycle Datapath: R-Type

## Slide 27
Write ALUResult to the register file
Add a MUX to choose between ReadData and ALUResult, we call the output Result.
MemtoReg = 0 for R-type to choose Result from the ALUResult, MemtoReg = 1 for lw to choose ReadData
Single-Cycle Datapath: R-Type

## Slide 28
For R-type instruction, the register to write is specified by the rd field, Instr15:11
  (for I-type instruction, the register to write is specified by the rt field, Instr20:16)
The MUX controlled by RegDst
RegDst= 1 for R-type to choose the rd field, Instr15:11;
RegDst = 0 for lw to choose the rt field, Instr20:16
Single-Cycle Datapath: R-Type

## Slide 29
beq $s0, $s1, target (if $s0 == $s1, jump to target)
If the values in rs and rt are equal, it takes the branch by adding the branch offset to the program counter
The offset is a positive or negative number, stored in the imm field of the instruction, Instr15:0. The offset indicates the no. of instructions to branch past.
Single-Cycle Datapath: beq

## Slide 30
The two registers are compared by computing SrcA – SrcB using the ALU.
If the ALUResult is 0, as indicated by the Zero flag from the ALU, the registers are equal.
Add a MUX to choose PC’ from either PCPlus4 or PCBranch
PCBranch is selected if the instruction is a branch and the Zero flag is asserted
Branch is 1 for beq, and 0 for others.
Single-Cycle Datapath: beq

## Slide 31
The immediate must be sign-extended ad multiplied by 4 to get the new program counter
PC’ = PC + 4 + SignImm x 4
PCBranch is computed by shifting SignImm left by 2 bits, then adding it to PCPlus4.
Single-Cycle Datapath: beq

## Slide 32
Single-Cycle Processor

## Slide 33
Single-Cycle Control

## Slide 34
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
Review: ALU

## Slide 35
Review: ALU

## Slide 36
ALUOp1:0 | Meaning
00 | Add
01 | Subtract
10 | Look at Funct
11 | Not Used
ALUOp1:0 | Funct | ALUControl2:0
00 | X | 010 (Add)
X1 | X | 110 (Subtract)
1X | 100000 (add) | 010 (Add)
1X | 100010 (sub) | 110 (Subtract)
1X | 100100 (and) | 000 (And)
1X | 100101 (or) | 001 (Or)
1X | 101010 (slt) | 111 (SLT)
Control Unit: ALU Decoder

## Slide 37
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 |  |  |  |  |  |  | 
lw | 100011 |  |  |  |  |  |  | 
sw | 101011 |  |  |  |  |  |  | 
beq | 000100 |  |  |  |  |  |  | 
Control Unit Main Decoder

## Slide 38
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
Control Unit: Main Decoder

## Slide 39
Single-Cycle Datapath: or

## Slide 40
No change to datapath
Extended Functionality: addi

## Slide 41
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 |  |  |  |  |  |  | 
Control Unit: addi

## Slide 42
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01
addi | 001000 | 1 | 0 | 1 | 0 | 0 | 0 | 00
Control Unit: addi

## Slide 43
Extended Functionality: j

## Slide 44
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 |  |  |  |  |  |  |  | 
Control Unit: Main Decoder

## Slide 45
Instruction | Op5:0 | RegWrite | RegDst | AluSrc | Branch | MemWrite | MemtoReg | ALUOp1:0 | Jump
R-type | 000000 | 1 | 1 | 0 | 0 | 0 | 0 | 10 | 0
lw | 100011 | 1 | 0 | 1 | 0 | 0 | 1 | 00 | 0
sw | 101011 | 0 | X | 1 | 0 | 1 | X | 00 | 0
beq | 000100 | 0 | X | 0 | 1 | 0 | X | 01 | 0
j | 000100 | 0 | X | X | X | 0 | X | XX | 1
Control Unit: Main Decoder

## Slide 46
Program Execution Time
= (#instructions)(cycles/instruction)(seconds/cycle)
= # instructions x CPI x TC
Review: Processor Performance

## Slide 47
TC limited by critical path (lw)
Other instructions have shorter critical paths
Each instruction in the single-cycle processor takes one clock cycle, so the CPI is 1
Single-Cycle Performance

## Slide 48
Single-cycle critical path:
Tc = tpcq_PC + tmem + max(tRFread, tsext + tmux) + tALU + tmem + tmux + tRFsetup
Typically, the ALU, memory, and register file accesses are substantially slower than other operations, the cycle time simplifies to
  Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
  The clock period is constant and must be long enough to accommodate the slowest instruction
Single-Cycle Performance

## Slide 49
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = ?
Single-Cycle Performance Example

## Slide 50
Element | Parameter | Delay (ps)
Register clock-to-Q | tpcq_PC | 30
Register setup | tsetup | 20
Multiplexer | tmux | 25
ALU | tALU | 200
Memory read | tmem | 250
Register file read | tRFread | 150
Register file setup | tRFsetup | 20
Tc = tpcq_PC + 2tmem + tRFread + tmux + tALU + tRFsetup
= [30 + 2(250) + 150 + 25 + 200 + 20] ps
= 925 ps
Single-Cycle Performance Example

## Slide 51
Program with 100 billion instructions:
Execution Time = # instructions x CPI x TC
= (100 × 109)(1)(925 × 10-12 s)
= 92.5 seconds
Single-Cycle Performance Example
A picosecond (ps) is 10−12 of a second
A nanosecond (ns) is 10−9 of a second
A microsecond (µs) is 10−6 of a second
A millisecond (ms) is 10−3 of a second