## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Prof. Peter Edwards
p.edwards@abdn.ac.uk
Notes: Some slides in this set adapted from:
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2: Logic Circuits

## Slide 3: From Logic to Gates
A schematic is a diagram of a digital circuit showing the elements and the wires that connect them together.
  Example: Y = ABC + ABC + ABC

## Slide 4: Circuit Schematic Rules
Inputs on the left (or top) of a schematic.
Outputs on right (or bottom) of a schematic.
Whenever possible, gates flow from left to right.
Straight wires are best!
Wires always connect at a T junction
  A dot where wires cross indicates a connection between the wires
  Wires crossing without a dot make no connection

## Slide 5: Example
  Y = ABC + ABC + ABC
  Y = BC + AB
simplification
Notes: The simplified circuit has significantly less hardware than the original one.
It may also be faster because of gates with fewer inputs

## Slide 6: Don’t Cares & Karnaugh Maps

## Slide 7: Multiple Output Circuits
Example: Priority Circuit Output asserted corresponding to
most significant TRUE input
A3
A2
A1
A0
Y3
Y2
Y1
Y0
PRIORITY CIRCUIT

## Slide 8: Priority Circuit

## Slide 9: Don’t Cares !
Here, symbol ‘X’ is used to indicate that we don’t care about the value of that variable.

## Slide 10: X’s & Z’s
Boolean algebra is limited to 0s and 1s.
However, real circuits can also have illegal and floating values, represented symbolically by X and Z.
Illegal Value: X
  The symbol X indicates that the circuit node has an unknown or illegal value.
Floating Value: Z
  The symbol Z indicates a node is being driven neither HIGH nor LOW.

## Slide 11: Contention (X)
Contention: Circuit tries to drive output to 1 and 0
  Actual value somewhere in between
  Could be 0, 1, or in forbidden zone
  Might change with voltage, temperature, time, noise
Warning!
  Contention usually indicates a bug.
  X is used for “don’t care” and contention - look at the context to tell them apart

## Slide 12: Karnaugh Maps (K-Maps)
Simplifying Boolean expressions via algebraic manipulation is hard since there is no uniform way of doing it …
Karnaugh map (or K-Map) technique is a commonly used graphical method.
  Another way to present truth table.
  Can represent Boolean functions of up to six variables.
K-Maps are tables of rows and columns with entries representing 1s or 0s of SOP and POS representations (minterms or maxterms).
Notes: From here onwards we will use minterms in our examples.

## Slide 13: K-Map Example
10
00
01
11
0
1
C
Y
AB
ABC
ABC
ABC
ABC
ABC
ABC
ABC
ABC
A B C Y
0 0 0 1
0 0 1 1
0 1 0 0
0 1 1 0
1 0 0 0
1 0 1 0
1 1 0 0
1 1 1 0
0
1
1
10
00
01
11
1
C
Y
AB
0
0
0
0
0
0
Y = AB

## Slide 14: K-Map
An n-variable K-Map has 2n cells with each cell corresponding to an n-variable truth table value.
K-Map cells are labeled with the corresponding truth-table row.
K-Map cells are arranged such that adjacent cells correspond to truth rows that differ in only one bit position (logical adjacency).
10
00
01
11
0
1
C
Y
AB
ABC
ABC
ABC
ABC
ABC
ABC
ABC
ABC
3 variables (A, B, C) – 23 (8) K-Map cells.
Differ by 1 bit: B vs B
Notes: Two terms containing an implicant P and the true and complementary forms of some variable A are combined to eliminate A:
PA + P notA = P

## Slide 15: K-Map Definitions
Complement: A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Prime implicant: implicant corresponding to the largest circle in a K-map

## Slide 16: K-Map Rules
Every 1 must be circled at least once
Each circle must span a power of 2 (i.e. 1, 2, 4) adjacent squares in each direction
Each circle must be as large as possible
A circle may wrap around the edges
A “don't care” (X) is circled only if it helps minimize the equation.

## Slide 17: 4-Input K-Map Example
Start, by drawing out the grid …
10
00
01
11
00
01
CD
Y
AB
11
10

## Slide 18: 4-Input K-Map Example
10
00
01
11
00
01
CD
Y
AB
11
10
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
Write the values of Y into the grid.

## Slide 19: 4-Input K-Map Example
Circle groups of 2, 4 or 8 adjacent squares.
Don’t forget wrap-around!
10
00
01
11
00
01
CD
Y
AB
11
10
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0

## Slide 20: 4-Input K-Map Example
10
00
01
11
00
01
CD
Y
AB
11
10
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
Y = AC + ABD + ABC + BD
0
10
00
01
11
00
01
CD
Y
AB
11
10
ABCD
0
0
0
0
0
0
ABCD
ABCD
ABCD
ABCD
ABCD
ABCD
ABCD
ABCD

## Slide 21: K-Maps with Don’t Cares

## Slide 22: K-Maps with Don’t Cares
Write in the values of the the function (Y) from the truth table.

## Slide 23: K-Maps with Don’t Cares
Circle groups of 2, 4 or 8 adjacent squares.
Notes: How do we arrive at solution?
Consider largest group of 8 squares (bottom 2 rows of grid):
not(A)not(B)CD not(A)BCD ABCD Anot(B)CD
not(A)not(B)Cnot(D) not(A)BCnot(D) ABCnot(D) Anot(B)Cnot(D)
This resolves into: C
Other largest group of 8 squares (3rd and 4th columns of grid):
ABnot(C)not(D) Anot(B)not(C)not(D)
ABnot(C)D Anot(B)not(C)D
ABCD Anot(B)CD
ABCnot(D) Anot(B)Cnot(D)
This resolves into: A
Last remaining circle includes the top-left square (not yet included) and also includes the other corner squares:
not(A)not(B)not(C)not(D)
Anot(B)Cnot(D)
Anot(B)not(C)not(D)
not(A)not(B)Cnot(D)
This resolves into: not(B)not(D)
GIVING FINAL RESULT:
A + not(B)not(D) + C