## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Prof. Peter Edwards
p.edwards@abdn.ac.uk
Notes: Some slides in this set adapted from:
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2: Combinational vs Sequential Logic

## Slide 3: Types of Logic Circuit
Combinational Logic
  Outputs determined by values of inputs
  No memory
  Lots of examples in last few lectures!
Sequential Logic
  Outputs depend on current and prior input values
  Has memory (short-term)

## Slide 4: Sequential Logic
Outputs of sequential logic depend on current and prior input values – it has memory.
Some definitions:
  State: all the information about a circuit necessary to explain its future behaviour
  Latches and flip-flops: state elements that store one bit of state
  Synchronous sequential circuits: combinational logic followed by a bank of flip-flops

## Slide 5: Combinational Logic

## Slide 6: Combinational Logic
Rules for combinational composition
  Every element in combinational
  Every node is either an input or connects to exactly one output.
  The circuit contains no cyclic paths
Example

## Slide 7: Combinational Circuits: Half Adder
Combinational logic circuits give us many useful devices.
One of the simplest is the half adder, which finds the sum of two bits.
Consider the truth table
  How might we build this?
X | Y | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Inputs
Outputs

## Slide 8: Half Adder
The sum can be found using the XOR operation and the carry using the AND operation.
Sum
Carry
X
Y
X | Y | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Inputs
Outputs

## Slide 9: Combinational Circuits: Full Adder
We can change our half adder into to a full adder by including gates for processing the carry bit.
Truth table for a full adder
X | Y | Carry In | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Inputs
Outputs

## Slide 10: Full Adder
How can we change the half adder shown below to make it a full adder?
X | Y | Carry In | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Inputs
Outputs
Sum
Carry
X
Y

## Slide 11: Full Adder
A completed full adder:
X | Y | Carry In | Sum | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Inputs
Outputs
Sum
Carry In
X
Y
Carry Out
Notes: Other types of combinational circuits:
decoders
multiplexers

## Slide 12: Ripple-Carry Adder
Just as we combined half adders to make a full adder, full adders can connected in series.
The carry bit “ripples” from one adder to the next; hence, this configuration is called a ripple-carry adder.
Notes: NB Today’s systems employ more efficient adders.

## Slide 13: Decoders
Decoders are another important type of combinational circuit.
Among other things, they are useful in selecting a memory location according to a binary value placed on the address lines of a memory bus.
Address decoders with n inputs can select any of 2n locations.
Decoder
•
•
•
•
•
•
2N outputs
N inputs
Notes: A combinational logic circuit that converts a binary integer value to an associated pattern of output bits. They are used in a wide variety of applications, including seven segment displays, and memory address decoding.

## Slide 14: 2:4 Decoder
Notes: One-hot output: only one output HIGH at once

## Slide 15: 2:4 Decoder Implementation
Implement a 2:4 decoder with AND, OR, and NOT gates.
In general, an N:2N decoder can be constructed from 2N N-input AND gates that accept the various combinations of true or complementary inputs.
Each output in a decoder represents a single minterm.
A1A0
A1A0
A1A0
A1A0

## Slide 16: Multiplexers
A multiplexer does just the opposite of a decoder.
It selects a single output from several inputs.
The particular input chosen for output is determined by the value of the multiplexer’s control lines.
To be able to select among n inputs, log2n control lines are needed.
Multiplexer (MUX)
Output
Control lines
S1
S2
I0
I1
I2
I3
Notes: An electronic multiplexer can be considered as a multiiple-input, single-output switch.
log2(4) = 2; log2(8) = 3 etc…

## Slide 17: Multiplexer (Mux)
Choose an output from among several possible inputs based on the value of a select signal.
Note the multiplexer symbol - a trapezoid showing inputs D0, D1 (left), output Y (right) and control S
S | Y
0 | D0
1 | D1
2:1 Mux
S | D0 | D1 | Y
0 | 0 | 0 | 0
0 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 1 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 1 | 1
D0
D1
Y
S
0
1
Notes: The schematic symbol for a multiplexer is an isosceles trapezoid with the longer parallel side containing the input pins and the short parallel side containing the output pin.
The schematic on the slideshows a 2-to-1 multiplexer .

## Slide 18: Multiplexer Implementation
A multiplexer can be built from SOP (sum-of-products) logic.
The Boolean equation may be derived with a K-map…
S | D0 | D1 | Y
0 | 0 | 0 | 0
0 | 1 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 1 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 1 | 1
0
0
1
1
1
1
0
0
10
00
01
11
0
1
S
Y
D0D1
Y = D0S + D1S
D0
D1
Y
S

## Slide 19: 4:1 Multiplexer
A 4:1 multiplexer has 4 data inputs and one output. Two select signals are needed to choose among the 4 data inputs.
Wider multiplexers, such as 8:1 and 16:1 can be built by expanding the model shown to the right.
In general an N:1 multiplexer needs log2N select lines.
S0S1D3
S0S1D2
S0S1D1
S0S1D0

## Slide 20: Logic Using Multiplexers
Multiplexers can be used as a lookup table to perform a logic function.
The 4:1 multiplexer shown to the right can be used to implement a 2-input AND gate.
  In general, a 2N input multiplexer can be programmed to perform any N-input logic function by applying 0’s and 1’s to the appropriate data inputs.
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
D0
D1
Y = AB
Y
A B
00
11
10
01

## Slide 21: Logic Using Multiplexers
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Y = AB
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Y = A + B
AND gate
XOR gate
A | Y
0 | 0
1 | B
A | Y
0 | B
1 | B
Y
A
0
1
B
Y
A
0
1
B
B

## Slide 22: Example – Logic with Mux
We need to implement the following function:
  Y = AB + BC + ABC
  We have a 4:1 multiplexer and an inverter.
  How do we implement the function?
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 23: Example – Logic with Mux
Solution:
  We reduce the truth table to 4 rows by letting the output depend on C.
    We can also choose to rearrange the columns of the truth table to let the output depend on A or B.
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
A | B | Y
0 | 0 | C
0 | 1 | C
1 | 0 | 1
1 | 1 | 0
Y
A B
00
11
10
01
C