## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Prof. Peter Edwards
p.edwards@abdn.ac.uk
Notes: Some slides in this set adapted from:
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2: Circuit Timings

## Slide 3: Timing
Delay between input change and output changing…
How to build fast circuits?
The blue arrow indicates that the rising edge of Y is caused by the rising edge of A.

## Slide 4: Propagation & Contamination Delay
Propagation delay: tpd = max delay from input to output
Contamination delay: tcd = min delay from input to output
Notes: Example is for a buffer

## Slide 5: Propagation & Contamination Delay
Delay is caused by
  Capacitance and resistance in a circuit
  Speed of light limitation
Reasons why tpd and tcd may be different:
  Different rising and falling delays
  Multiple inputs and outputs, some of which are faster than others.
  Circuits slow down when hot and speed up when cold.

## Slide 6: Critical (Long) & Short Paths
Critical (Long) Path: tpd = 2 x tpd_AND + tpd_OR
Short Path: tcd = tcd_AND

## Slide 7: Sequential Logic

## Slide 8: Sequential Circuits
Combinational logic circuits are perfect for situations when we require the immediate application of a Boolean function to a set of inputs.
There are other times, however, when we need a circuit to change its value with consideration to its current state as well as its inputs.
  These circuits have to “remember” their current state.
Sequential logic circuits provide this functionality for us.
Notes: Sequential logic is used to construct finite state machines (FSMs) - a basic building block in all digital circuitry, as well as memory circuits and other devices. Virtually all circuits in practical digital devices are a mixture of combinational and sequential logic

## Slide 9: Sequential Circuits
As the name implies, sequential logic circuits require a means by which events can be sequenced.
State changes are controlled by clocks.
  A “clock” is a special circuit that sends electrical pulses through a circuit.
Clocks produce electrical waveforms such as the one shown below.

## Slide 10: Sequential Circuits
State changes occur in sequential circuits only when the clock ticks.
Circuits can change state on the rising edge, falling edge, or when the clock pulse reaches its highest voltage.
Notes: Circuits that change state on the rising edge, or falling edge of the clock pulse are called edge-triggered.
Level-triggered circuits change state when the clock voltage reaches its highest or lowest level.

## Slide 11: Sequential Circuits
To retain their state values, sequential circuits rely on feedback.
Feedback in digital circuits occurs when an output is looped back to the input.
A simple example of this concept is shown below.
  Bistable circuit - a fundamental building block.
  No inputs, 2 outputs: Q, Q
  If Q is 0 it will always be 0, if it is 1, it will always be 1. Why?

## Slide 12: Bistable Circuit
Consider the two possible cases: Q = 0: then Q = 1, Q = 0 (consistent) Q = 1: then Q = 0, Q = 1 (consistent)
  Two stable states, Q=0 and Q=1,
  the circuit is said to be bistable
Stores 1 bit of state in the state variable, Q (or Q)
But there are no inputs to control the state

## Slide 13: SR (Set/Reset Latch)
We can see how feedback works by examining the most basic sequential logic components, the SR latch
  “SR” stands for set/reset.
The internals of an SR latch are shown below:
Notes: Latches and flip-flops are the basic elements for storing information. One latch or flip-flop can store one bit of information. The main difference between latches and flip-flops is that for latches, their outputs are constantly affected by their inputs as long as the enable signal is asserted. In other words, when they are enabled, their content changes immediately when their inputs change. Flip-flops, on the other hand, have their content change only either at the rising or falling edge of the enable signal. This enable signal is usually the controlling clock signal. After the rising or falling edge of the clock, the flip-flop content remains constant even if the input changes.

## Slide 14: SR Latch Analysis
  S = 1, R = 0: then Q = 1 and Q = 0
  S = 0, R = 1: then Q = 1 and Q = 0
Notes: Consider the four possible cases:
  S = 1, R = 0
  S = 0, R = 1
  S = 0, R = 0
  S = 1, R = 1

## Slide 15: SR Latch Analysis
  S = 0, R = 0: then Q = Qprev
  S = 1, R = 1: then Q = 0 and Q = 0
MEMORY!
Invalid State
Q ≠ NOT Q
Notes: Asserting both S and R simultaneously doesn’t make much sense, because it means the latch should be set and reset at the same time, which is impossible

## Slide 16: SR Latch Analysis
The behaviour of an SR latch is described by a characteristic table.
  Q(t) means the value of the output at time t. Q(t+1) is the value of Q after the next clock pulse.
S | R | Q (t+1)
0 | 0 | Q(t)
0 | 1 | 0 (reset to 0)
1 | 0 | 1 (set to 1)
1 | 1 | undefined
Remember: SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1 (S = 1, R = 0, Q = 1)
  Reset: Make the output 0 (S = 0, R = 1, Q = 0)

## Slide 17: SR Latch Analysis
The SR latch actually has three inputs: S, R, and its current output, Q.
Thus, we can construct a truth table for this circuit, as shown at the right.
Notice the two undefined values. When both S and R are 1, the SR latch is unstable.
S | R | Q(t) | Q (t+1)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | undefined
1 | 1 | 1 | undefined
Must do something to avoid invalid state.

## Slide 18: SR Latch
SR Latch is a bistable circuit with 1 bit of state stored in Q.

## Slide 19: SR Latch Exercise
Given the input waveforms shown below, sketch the output Q, of an SR latch:
Remember the rules for behaviour of the SR latch.
1
0
1
0
0
1
0
1
0
1
0
0
1

## Slide 20: SR Latch Exercise
1
0
1
0
0
1
0
1
0
1
0
0
1
S=1, R=0 => Q=1
S=0, R=1 => Q=0
S=1, R=0 => Q=1
S=0, R=0 => Q=Qprev
Notes: What is Qprev at the start ? We don’t know – so plot shows Q=1 and Q=0 for the initial segment….

## Slide 21: D Latch
Two inputs: CLK, D
  CLK: controls when the output changes
  D (the data input): controls what the output changes to
Function
  When CLK = 1, D passes through to Q (transparent)
  When CLK = 0, Q holds its previous value (opaque)
Avoids invalid case when Q ≠ NOT Q
Notes: The disadvantage with the SR latch is that we need to ensure that the two inputs, S and R, are never set at the same time. This situation is prevented in the D latch by adding an inverter and replacing S and R with just one input D (for data)
CLK = clock

## Slide 22: D Latch
When CLK = 1, the latch is transparent. Q = D (just like a buffer)
When CLK = 0, the latch is opaque. Q retains old value.
CLK | D | D | S | R | Q | Q
0 | X | X | 0 | 0 | Qprev | Qprev
1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0

## Slide 23: D Latch Exercise
Given the input waveforms shown below, sketch the output Q, of a D latch:
1
0
1
0
0
1
1
0
1
0
1
0
0
1
1

## Slide 24: D Latch Exercise
1
0
1
0
0
1
1
0
1
0
1
0
0
1
1
clk=0, D=0 => Q=Qprev
clk=1, D=1 => Q=1
clk=1, D=0 => Q=0
clk=1, D=1 => Q=1