## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Prof. Peter Edwards
p.edwards@abdn.ac.uk
Notes: Some slides in this set adapted from:
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2: Sequential Logic contd…

## Slide 3: Latches vs Flip-Flops
Latches are “transparent”
  Any change on the inputs is seen at the outputs immediately when CLK=1.
  This causes synchronization problems.
Solution: Use latches to create flip-flops that can respond (update) only at specific times (instead of any time).
Flip-Flop
  Output only changes according to behaviour of clock edge.
  Also known as clocked devices.
D Flip-Flop
  The fundamental circuit of computer memory.
Notes: Clocked devices are specially designed for synchronous systems; such devices ignore their inputs except at the transition of a dedicated clock signal (known as clocking, pulsing, or strobing)
“D” in D Flip-Flop stands for “data” or “delay”

## Slide 4: D Flip-Flop
Two inputs: CLK, D
Function
  Samples D on rising edge of CLK
    When CLK rises from 0 to 1, D passes through to Q
    Otherwise, Q holds its previous value
Q changes only on rising edge of CLK
  Called edge-triggered
  Activated on the clock edge.
Notes: Another type of flip-flop: JK flip-flop
A JK flip-flop receives a clock and two inputs, J and K. On the rising edge of the clock, it updates the output, Q.
If J and K are both 0, Q retains its old value.
If only J is 1, Q becomes 1.
If only K is 1, Q becomes 0.
If J and K are both 1, Q becomes the opposite of its present state.

## Slide 5: D Flip-Flop
Truth table:
D input specifies what the new state will be.
The clock edge indicates when the state should be updated.
CLK | D | Q
Rising edge | 0 | 0
Rising edge | 1 | 1
Non-rising | X | Qprev
Notes: Remember ‘X’ in the truth table = don’t care!

## Slide 6: D Flip-Flop
Two back-to-back latches (L1 and L2) controlled by complementary clocks
When CLK = 0
L1 is transparent
L2 is opaque
D passes through to N1
When CLK = 1
L2 is transparent
L1 is opaque
N1 passes through to Q
Thus, on the edge of the clock (when CLK rises from 0 to 1)
D passes through to Q

## Slide 7: D Latch vs D Flip-Flop
1
0
1
0
0
1
0
1
0
0
1
1
Remember
D latch is level-sensitive; D latch is transparent when CLK = 1
D flip-flop is edge triggered, D flip-flop copies D to Q on the rising edge of CLK
At all other times, both retain their old state.

## Slide 8: D Latch vs D Flip-Flop
1
0
1
0
0
1
0
1
0
0
1
1
1
0
0
1
1
0
Notes: Remember
D latch is level-sensitive; D latch is transparent when CLK = 1
D flip-flop is edge triggered, D flip-flop copies D to Q on the rising edge of CLK
At all other times, both retain their old state.

## Slide 9: Registers
An N-bit register is a bank of N flip-flops that share a common clock input, so that all bits of the register are updated at the same time.

## Slide 10: Flip-Flop Variants
Enabled Flip-Flop
  Three inputs: CLK, D, EN
Function
  EN = 1: D passes through to Q on the clock edge
  EN = 0: The flip-flop retains its previous state
  Enable input (EN) controls when new data (D) is stored.
Useful when we wish to load a new value into a flip-flop only some of the time, rather than on every clock edge.

## Slide 11: Flip-Flop Variants
Resettable Flip-Flop
  Three inputs: CLK, D, Reset
Function
  Reset = 1: Q is forced to 0
  Reset = 0: flip-flop behaves as ordinary D flip-flop
Useful when we want to force a known state (i.e. 0) into all the flip-flops in a system when we first turn it on.

## Slide 12: Resettable Flip-Flops
Two types:
  Synchronous: resets at the clock edge only
  Asynchronous: resets immediately when Reset = 1
Asynchronously resettable flip-flop requires changing the internal circuitry of the flip-flop.

## Slide 13: Settable Flip-Flops
Three inputs: CLK, D, Set
Function
  Set = 1: Q is set to 1
  Set = 0: The flip-flop behaves as ordinary D flip-flop

## Slide 14: A Problematic Circuit
Remember:
  A sequential circuit is any circuit that is not combinational.
How does this problematic circuit behave?

## Slide 15: A Problematic Circuit
No inputs and 1-3 outputs
Astable circuit, oscillates
Period depends on inverter delay
It has a cyclic path: output fed back to input

## Slide 16: Synchronous Sequential Logic Design
Break cyclic paths by inserting registers
Registers contain state of the system
State changes at clock edge:
  system synchronized to the clock.
Rules of synchronous sequential circuit composition:
  Every circuit element is either a register or a combinational circuit.
  At least one circuit element is a register.
  All registers receive the same clock signal.
  Every cyclic path contains at least one register.
Notes: There are two types of sequential circuits:
Synchronous sequential circuit: circuit output changes only at some discrete instants of time. This type of circuits achieves synchronization by using a timing signal called the clock.
Asynchronous sequential circuit: circuit output can change at any time (clockless).

## Slide 17: Finite State Machines
So far, our sequential circuit outputs have been limited to state variables (e.g. Q)
In general, sequential circuits have outputs in addition to the state variable(s).
Two types (or models) of sequential circuits (FSMs):
  Mealy Machine
    Output is a function of present state and present input
  Moore Machine
    Output is a function of present state only

## Slide 18: FSM Example: Coin-Operated Turnstile
Locked
Un locked
Coin
Push
Push
Coin
Current State | Input | Next State | Output
Locked | coin | Unlocked | Unlock so customer can push through
Locked | push | Locked | None
Unlocked | coin | Unlocked | None
Unlocked | push | Locked | When customer pushes through, lock
State transition table
State diagram
Notes: Initially the arms are locked, blocking the entry, preventing patrons from passing through.
Depositing a coin or token in a slot on the turnstile unlocks the arms, allowing a single customer to push through.
After the customer passes through, the arms are locked again until another coin is inserted.
Considered as a state machine, the turnstile has two states: Locked and Unlocked.
There are two inputs that affect its state: putting a coin in the slot (coin) and pushing the arm (push).
In the locked state, pushing on the arm has no effect; no matter how many times the input push is given, it stays in the locked state.
Putting a coin in – that is, giving the machine a coin input – shifts the state from Locked to Unlocked.
In the unlocked state, putting additional coins in has no effect; that is, giving additional coin inputs does not change the state.
However, a customer pushing through the arms, giving a push input, shifts the state back to Locked.