## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 3 – Sequential Logic
David Money Harris and Sarah L. Harris

## Slide 2
Chapter 3 :: Topics
Finite State Machines

## Slide 3: Sequential Circuits
Sequential circuits are used anytime that we have a “stateful” application.
A stateful application is one where the next state of the machine depends on the current state of the machine and the input.
A stateful application requires both combinational and sequential logic.

## Slide 4: Finite State Machines
The behaviour of sequential circuits can be expressed using finite state machines (FSMs).
An FSM:
  Takes an input and a current state.
  Produces an output and a new state.
It is called a Finite State Machine because it can have, at most, a finite number of states.
It is composed of combinational logic components and flip-flops placed in such a way as to maintain state information.

## Slide 5: Finite State Machines
FSMs can be represented by a set of nodes that hold the states of the machine and a set of arcs that connect the states.
Q=0
Q=1
D=1
D=1
D=0
D=1
A circle with the state name in it for each state.
A directed arc from the Present State to the Next State for each state transition.
A label on each directed arc with the input values which causes the state transition.
A label:
On each circle with the output value produced, or
On each directed arc with the output value produced.
Notes: The state diagram shown is that for a D flip-flop.
BUT note that the diagram does not indicate *when* the transitions take place. For a D flip-flop it is of course on the clock rising edge.

## Slide 6: Finite State Machines
Moore and Mealy machines are two types of FSMs that are equivalent.
They differ only in how they express the outputs of the machine.
  Mealy FSM: outputs depend on current state and inputs
  Moore FSM: outputs depend only on current state

## Slide 7: Finite State Machines
Consist of:
  State register
    Stores current state
    Loads next state at clock edge
  Combinational logic
    Computes the next state
Consist of:
  State register
    Stores current state
    Loads next state at clock edge
  Combinational logic
    Computes the outputs

## Slide 8
Traffic light controller
  Traffic sensors: TA, TB (TRUE when there’s traffic)
  Lights: LA, LB
FSM Example

## Slide 9
Inputs: CLK, Reset, TA, TB
Outputs: LA, LB
FSM Black Box

## Slide 10
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs
FSM State Transition Diagram

## Slide 11
Moore FSM: outputs labeled in each state
States: Circles
Transitions: Arcs
FSM State Transition Diagram

## Slide 12
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | 
S0 | 1 | X | 
S1 | X | X | 
S2 | X | 0 | 
S2 | X | 1 | 
S3 | X | X | 
FSM State Transition Table

## Slide 13
Current State | Inputs |  | Next State
S | TA | TB | S'
S0 | 0 | X | S1
S0 | 1 | X | S0
S1 | X | X | S2
S2 | X | 0 | S3
S2 | X | 1 | S2
S3 | X | X | S0
FSM State Transition Table

## Slide 14
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X |  | 
0 | 0 | 1 | X |  | 
0 | 1 | X | X |  | 
1 | 0 | X | 0 |  | 
1 | 0 | X | 1 |  | 
1 | 1 | X | X |  | 
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
FSM Encoded State Transition Table

## Slide 15
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S'1 | S'0
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
S3 | 11
S'1 = S1 Å S0
S'0 = S1S0TA + S1S0TB
FSM Encoded State Transition Table

## Slide 16
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 |  |  |  | 
0 | 1 |  |  |  | 
1 | 0 |  |  |  | 
1 | 1 |  |  |  | 
Output | Encoding
green | 00
yellow | 01
red | 10
FSM Output Table

## Slide 17
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
green | 00
yellow | 01
red | 10
LA1 = S1
LA0 = S1S0
LB1 = S1
LB0 = S1S0
FSM Output Table

## Slide 18
FSM Schematic: State Register

## Slide 19
FSM Schematic: Next State Logic

## Slide 20
FSM Schematic: Output Logic

## Slide 21
FSM Timing Diagram

## Slide 22
Binary encoding:
  i.e., for four states, 00, 01, 10, 11
One-hot encoding
  One state bit per state
  Only one state bit HIGH at once
  i.e., for 4 states, 0001, 0010, 0100, 1000
  Requires more flip-flops
  Often next state and output logic is simpler
FSM State Encoding

## Slide 23: FSM Example: Paper Tape
A snail that crawls down a paper tape with 1’s and 0’s on it. The snail smiles whenever the last two digits it has crawled over are 01.
How do we design Moore and Mealy FSMs of the snail’s brain?
Let’s begin with the Moore version …

## Slide 24
Mealy FSM: arcs indicate input/output
State Transition Diagrams

## Slide 25
Current State |  | Inputs | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
State | Encoding
S0 | 00
S1 | 01
S2 | 10
Moore FSM State Transition Table

## Slide 26
Current State |  | Inputs | Next State | 
S1 | S0 | A | S'1 | S'0
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
State | Encoding
S0 | 00
S1 | 01
S2 | 10
Moore FSM State Transition Table
S1’ = S0A
S0’ = A

## Slide 27
Current State |  | Output
S1 | S0 | Y
0 | 0 | 
0 | 1 | 
1 | 0 | 
Y = S1
Moore FSM Output Table

## Slide 28
Current State |  | Output
S1 | S0 | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
Y = S1
Moore FSM Output Table

## Slide 29
Current State | Input | Next State | Output
S0 | A | S'0 | Y
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
State | Encoding
S0 | 00
S1 | 01
Mealy FSM State Transition & Output Table

## Slide 30
Current State | Input | Next State | Output
S0 | A | S'0 | Y
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
State | Encoding
S0 | 00
S1 | 01
Mealy FSM State Transition & Output Table

## Slide 31
Moore FSM Schematic

## Slide 32
Mealy FSM Schematic

## Slide 33
Moore & Mealy Timing Diagram

## Slide 34
Identify inputs and outputs
Sketch state transition diagram
Write state transition table
Select state encodings
For Moore machine:
  Rewrite state transition table with state encodings
  Write output table
For a Mealy machine:
  Rewrite combined state transition and output table with state encodings
Write Boolean equations for next state and output logic
Sketch the circuit schematic
FSM Design Procedure