## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Prof. Peter Edwards
p.edwards@abdn.ac.uk
Notes: Some slides in this set adapted from:
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2: Finite State Machines

## Slide 3: Sequential Circuits
Sequential circuits are used anytime that we have a “stateful” application.
A stateful application is one where the next state of the machine depends on the current state of the machine and the input.
A stateful application requires both combinational and sequential logic.

## Slide 4: Finite State Machines
The behaviour of sequential circuits can be expressed using finite state machines (FSMs).
An FSM:
  Takes an input and a current state.
  Produces an output and a new state.
It is called a Finite State Machine because it can have, at most, a finite number of states.
It is composed of combinational logic components and flip-flops placed in such a way as to maintain state information.

## Slide 5: Finite State Machines
FSMs can be represented by a set of nodes that hold the states of the machine and a set of arcs that connect the states.
Q=0
Q=1
D=1
D=1
D=0
D=1
A circle with the state name in it for each state.
A directed arc from the Present State to the Next State for each state transition.
A label on each directed arc with the input values which causes the state transition.
A label:
On each circle with the output value produced, or
On each directed arc with the output value produced.
Notes: The state diagram shown is that for a D flip-flop.
BUT note that the diagram does not indicate *when* the transitions take place. For a D flip-flop it is of course on the clock rising edge.

## Slide 6: Finite State Machines
Moore and Mealy machines are two types of FSMs that are equivalent.
They differ only in how they express the outputs of the machine.
  Mealy FSM: outputs depend on current state and inputs
  Moore FSM: outputs depend only on current state

## Slide 7: Finite State Machines
Consist of:
  State register
    Stores current state
    Loads next state at clock edge
  Combinational logic
    Computes the next state
Consist of:
  State register
    Stores current state
    Loads next state at clock edge
  Combinational logic
    Computes the outputs

## Slide 8: FSM Example: Traffic Management
Traffic light controller
  Traffic sensors: TA, TB
    TRUE if traffic detected
  Lights: LA, LB
Bon Accord St
Union St
Union St
Union Row
TA
TA
TB
TB
LA
LA
LB
LB

## Slide 9: FSM ‘Black Box’
Inputs: CLK, Reset, TA, TB
Outputs: LA, LB

## Slide 10: State Transitions
LB
Bon Accord St
Union St
Union St
Union Row
TA
TA
TB
TB
LA
LA
LB
LB
Bon Accord St
Union St
Union St
Union Row
TA
TA
TB
TB
LA
LA
LB
Initial State: UR-BA-Green
TA = 0 (no vehicles detected)
Next State: UR-BA-Amber
Notes: This slides shows the first 2 states – State 0 and State 1; need to do the same for other states to generate state diagram – see next slide…

## Slide 11: State Diagram
States: Circles
Transitions: Arcs
Moore FSM: outputs labeled in each state
Reset
TA
UR-BA-
Green
LA: green LB: red
UR-BA-
Amber
LA: amber LB: red
UNIONST-
Green
LA: red LB: green
UNIONST-Amber
LA: red LB: amber
TB
TB
TA

## Slide 12: State Transition Table
Current State (S) | TA | TB | Next State (S’)
UR-BA-Green | 0 | X | 
UR-BA-Green | 1 | X | 
UR-BA-Amber | X | X | 
UNIONST-Green | X | 0 | 
UNIONST-Green | X | 1 | 
UNIONST-Amber | X | X | 
State | Encoding
UR-BA-Green | 00
UR-BA-Amber | 01
UNIONST-Green | 10
UNIONST-Amber | 11
UR-BA-Amber
UR-BA-Green
UNIONST-Green
UNIONST-Amber
UNIONST-Green
UR-BA-Green
This is a conventional state transition table.
Our next step is to rewrite in a form more suited to analysis – by using binary coding for each state instead of symbols
State Encoding
Notes: Symbolic states are assigned bit codes
codes can be arbitrarily chosen
some are better than others (“optimal state coding”)

## Slide 13: Encoded State Transition Table
Using the state encoding gives us:
Current State |  | Inputs |  | Next State | 
S1 | S0 | TA | TB | S1’ | S0’
0 | 0 | 0 | X | 0 | 1
0 | 0 | 1 | X | 0 | 0
0 | 1 | X | X | 1 | 0
1 | 0 | X | 0 | 1 | 1
1 | 0 | X | 1 | 1 | 0
1 | 1 | X | X | 0 | 0
S0, S1, etc. refer to the bits of the state encoding
S'1 = S1 + S0
S'0 = S1S0TA + S1S0TB
Next State Logic:
Notes: Next state logic reflects the logic of state transitions.

## Slide 14: Output Table
We now need to consider the output logic.
Begin by bit encoding the outputs:
Create output table:
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output | Encoding
Green | 00
Amber | 01
Red | 10
UR-BA-Green
Notes: Inputs and outputs assigned bit codes
again, codes can be arbitrarily chosen
again, some are better than others
UR-BA-Green is shown; other rows correspond to other states.

## Slide 15: Output Table
Current State |  | Outputs |  |  | 
S1 | S0 | LA1 | LA0 | LB1 | LB0
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1
Output Logic:
LA1 = S1
LA0 = S1S0
LB1 = S1
LB0 = S1S0

## Slide 16: Designing the FSM Schematic
STEP 1:
  Consider the management of state information.
Notes: Two state variables to handle (use 2 flip-flops).

## Slide 17: FSM Schematic: Next State Logic
STEP 2:
S'1 = S1 + S0
S'0 = S1S0TA + S1S0TB
Next State Logic:
Notes: The logic diagram corresponds to the next state logic we identified earlier.

## Slide 18: FSM Schematic: Output Logic
STEP 3:
Output Logic:
LA1 = S1
LA0 = S1S0
LB1 = S1
LB0 = S1S0
Notes: Again, the output logic circuit follows from the output logic identified earlier.

## Slide 19: FSM Timing Diagram
S0 = UR-BA-Green (00)
S1 = UR-BA-Amber (01)
S2 = UNIONST-Green (10)
S3 = UNIONST-Amber (11)

## Slide 20: Review of FSM Design Stages
Specify circuit function in terms of inputs and outputs (English)
Sketch state transition diagram
Write state transition table
Select state encodings
For Moore machine: 5.1 Rewrite state transition table with state encodings 5.2 Write output table
For a Mealy machine: 6.1 Rewrite combined state transition and output table with state encodings
Write Boolean equations for next state and output logic
Sketch the circuit schematic Register(s) to hold state Combinational Logic for Next State and Outputs

## Slide 21: State Encoding
In general:
  Number of possible FSM states = 2number of flip-flops
  However, often more than log2(number of states) flip-flops are used, to simplify logic at the cost of more flip-flops.
  Example is one-hot state encoding.

## Slide 22: State Encoding
One-hot encoding:
  One state bit per state
  Only one state bit HIGH at once
    e.g. for 4 states, 0001, 0010, 0100, 1000
  Requires more flip-flops
    e.g. for 4 states above: 1 flip-flop per state
  But: often next state and output logic is simpler.
Notes: How to use as few states as possible?
State minimization is a well-studied problem
It is a tough problem (NP-complete)
but pretty good algorithms exist
- Exact and approximate
- Out of the scope of this course

## Slide 23: FSM Example: Paper Tape
A snail that crawls down a paper tape with 1’s and 0’s on it. The snail smiles whenever the last two digits it has crawled over are 01, else it frowns.
How do we design Moore and Mealy FSMs of the snail’s brain?
Let’s begin with the Moore version …

## Slide 24: Paper Tape – Moore FSM
Reset
1
Reading State 0
Y: frown
Reading State 1
Y: frown
Reading
State 2
Y: smile
0
1
0
0
1
State | Encoding
Reading State0 | 00
Reading State1 | 01
Reading State2 | 10
State Encoding:

## Slide 25: Paper Tape – Moore FSM
S1’ = S0A
S0’ = A
Current State |  | Inputs | Next State | 
S1 | S0 | A | S1’ | S0’
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
State Transition Table:
Next State Logic:

## Slide 26: Paper Tape – Moore FSM
Current State |  | Output
S1 | S0 | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
Output (Y) | Encoding
frown | 0
smile | 1
Output Logic:
Y = S1
Output Encoding:
Output Table:

## Slide 27: Result: Moore FSM Schematic
S1’ = S0A
S0’ = A
Next State Logic:
Output Logic:
Y = S1

## Slide 28: Paper Tape – Mealy FSM
Reset
1/0
Reading State0
Reading State 1
0/0
0/0
1/1
NOTE!
Mealy FSM: arcs indicate input/output
1 = smile; 0 = frown
State | Encoding
Reading State0 | 00
Reading State1 | 01
State Encoding:

## Slide 29: Paper Tape – Mealy FSM
Current State | Inputs | Next State | Output
S0 | A | S0’ | Y
0 | 0 | 1 | 0
0 | 1 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
State Transition & Output Table:
Output Logic:
Y = S0 A
S0’ = A
Next State Logic:

## Slide 30: Result: Mealy FSM Schematic
Output Logic:
Y = S0 A
S0’ = A
Next State Logic: