## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Prof. Peter Edwards
p.edwards@abdn.ac.uk
Notes: Some slides in this set adapted from:
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2: Finite State Machines

## Slide 3: FSM Example: Paper Tape #2
The snail from our earlier example has a daughter with a Mealy machine brain.
  The daughter snail smiles whenever she slides over the pattern 1101 or the pattern 1110.
Question:
  Sketch the state transition diagram for this happy snail using as few states as possible.
  Choose state encodings and write a combined state transition and output table using your encodings.
  Write the next state and output equations and sketch your FSM schematic.

## Slide 4: Paper Tape #2 - Mealy FSM
Reset
0/0
Reading State0
1/0
0/0
0/1
Reading State1
Reading State2
Reading State3
Reading State4
0/0
0/0
1/0
1/0
1/0
1/1
The daughter snail smiles whenever she slides over the pattern 1101 or the pattern 1110.

## Slide 5: Paper Tape #2 - Mealy FSM
State | Encoding (s2:0)
Reading State0 | 000
Reading State1 | 001
Reading State2 | 010
Reading State3 | 100
Reading State4 | 101
State Encoding:

## Slide 6: Paper Tape #2 - Mealy FSM
Current State |  |  | Inputs | Next State |  |  | Output
S2 | S1 | S0 | A | S2’ | S1’ | S0’ | Q
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
State Transition & Output Table:
The daughter snail smiles whenever she slides over the pattern 1101 or the pattern 1110.

## Slide 7: Paper Tape #2 - Mealy FSM
Derive Next State Logic:
00
01
S0A
S2S1
11
10
S0’
0
0
1
1
-
0
0
-
0
1
-
0
-
-
1
-
00
01
11
10
S2S0A
+ S2S1A
Current State |  |  | Inputs | Next State |  |  | Output
S2 | S1 | S0 | A | S2’ | S1’ | S0’ | Q
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0

## Slide 8: Paper Tape #2 - Mealy FSM
Derive Next State Logic:
00
01
S0A
S2S1
11
10
S0’
0
0
1
1
-
0
0
-
0
1
-
0
-
-
1
-
00
01
11
10
00
01
S0A
S2S1
11
10
S1’
0
0
0
0
-
1
0
-
0
0
-
0
-
-
0
-
00
01
11
10
S2S1S0A
S2S0A
+ S2S1A
00
01
S0A
S2S1
11
10
S2’
0
0
1
0
-
0
0
-
1
1
-
1
-
-
0
-
00
01
11
10
+ S2S1S0
S2S1S0

## Slide 9: Paper Tape #2 - Mealy FSM
Derive Output Logic:
00
01
S0A
S2S1
11
10
Q
0
0
0
1
-
0
0
-
1
0
-
0
-
-
0
-
00
01
11
10
S2S1S0A + S2S1S0A
Current State |  |  | Inputs | Next State |  |  | Output
S2 | S1 | S0 | A | S2’ | S1’ | S0’ | Q
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0

## Slide 10: Result: Mealy FSM Schematic (PaperTape#2)
Output Logic:
Q = S2S1S0A + S2S1S0A
Next State Logic:
S0’ = S2S0A + S2S1A
S1’ = S2S1S0A
S2’ = S2S1S0 + S2S1S0

## Slide 11: Timings

## Slide 12: Timing
Remember:
  Flip-flop samples D at clock edge
D must be stable when sampled
Similar to a photograph, D must be stable around clock edge.
Aperture time – during which the object must remain still for a sharp image to be captured.
The aperture of a sequential element – a setup time and a hold time, before and after the clock edge, respectively.

## Slide 13: Input Timing Constraints
Setup time:
  tsetup = time before clock edge data must be stable (i.e. not changing)
Hold time:
  thold = time after clock edge data must be stable
Aperture time:
  ta = time around clock edge data must be stable (ta = tsetup + thold)

## Slide 14: Output Timing Constraints
Propagation delay: tpcq = time after clock edge that the output Q is guaranteed to be stable (i.e., to stop changing)
Contamination delay: tccq = time after clock edge that Q might be unstable (i.e., start changing)
Notes: NOTE:
Compare with propagation delay (tpd) and contamination delay (tcd) of a logic gate – see earlier in the course.
Propagation delay and contamination delay on *this* slide are definitions of those terms for sequential circuits….
Propagation delay - This value indicates the amount of time needed for a change in the flip flop-clock input (e.g. rising edge) to result in a permanent change at the flip-flop output (Q). When the clock edge arrives, the D input value is transfered to output Q. The output of the flip-flop may be at an intermediate value for a while (indicated by the cross-hatched area) before the final output value is created. After tpcq, the output is guaranteed not to change value again until another clock edge trigger (e.g. rising edge) arrives.
Contamination delay - This value indicates the amount of time needed for a change in the flip-flop clock input to result in the initial change at the flip-flop output (Q). The output of the flip-flop maintains its initial value until time tccq has passed. The flip-flop is guaranteed not to show any output change in response to an input change until after tcd has passed.

## Slide 15: Dynamic Discipline
Synchronous sequential circuit inputs must be stable during aperture (setup and hold) time around clock edge.
Specifically, inputs must be stable:
  at least tsetup before the clock edge.
  at least until thold after the clock edge.

## Slide 16: Dynamic Discipline
The delay between registers has a minimum and maximum delay, dependent on the delays of the circuit elements.

## Slide 17: Setup Time Constraint (Tc)
Depends on the maximum delay from register R1 through combinational logic to R2.
The input to register R2 must be stable at least tsetup before clock edge.
Tc ≥ tpcq + tpd + tsetup
tpd ≤ Tc – (tpcq + tsetup)
Notes: REMEMBER: tpcq = time after clock edge that the output Q is guaranteed to be stable (i.e., to stop changing)

## Slide 18: Hold Time Constraint
Depends on the minimum delay from register R1 through the combinational logic to R2.
The input to register R2 must be stable for at least thold after the clock edge.
thold < tccq + tcd
tcd > thold - tccq
Notes: REMEMBER
tccq = time after clock edge that Q might be unstable (i.e., start changing)

## Slide 19: Timing Analysis
Timing Characteristics
tccq = 30 ps
tpcq = 50 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
per gate
tpd = 3 x 35 ps = 105 ps
tcd = 25 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 25) ps > 70 ps ? No!

## Slide 20: Timing Analysis
per gate
Timing Characteristics
tccq = 50 ps
tpcq = 70 ps
tsetup = 60 ps
thold = 70 ps
tpd = 35 ps
tcd = 25 ps
tpd = 3 x 35 ps = 105 ps
tcd = 2 x 25 ps = 50 ps
Setup time constraint:
Tc ≥ (50 + 105 + 60) ps = 215 ps
fc = 1/Tc = 4.65 GHz
Hold time constraint:
tccq + tcd > thold ?
(30 + 50) ps > 70 ps ? Yes!
Buffers added to the short paths:

## Slide 21: Timing Analysis - Example
Each two input XOR gate has a propagation delay of 100ps and a contamination delay of 55ps.
Each flip-flop has a setup time of 60ps, a hold time of 20ps, a clock-to-Q maximum delay of 70ps, and a clock-to-Q minimum delay of 50ps.
What is the maximum operating frequency of the circuit?

## Slide 22: Timing Analysis - Example
per gate
Timing Characteristics
tccq = 50 ps
tpcq = 70 ps
tsetup = 60 ps
thold = 20 ps
tpd = 100 ps
tcd = 55 ps
tpd = 3 x 100 ps = 300 ps
tcd = 1 x 55 ps = 55 ps
Setup time constraint:
Tc ≥ (70 + 300 + 60) ps = 430 ps
fc = 1/Tc = 2.33 GHz
Hold time constraint:
tccq + tcd > thold ?
(50 + 55) ps > 20 ps ? Yes!