## Slide 1: CS 1520 COMPUTER ARCHITECTURE
Prof. Peter Edwards
p.edwards@abdn.ac.uk
Notes: Some slides in this set adapted from:
Digital Design and Computer Architecture, 2nd Edition
David Money Harris and Sarah L. Harris

## Slide 2: Digital Building Blocks

## Slide 3: Digital Building Blocks
Gates, multiplexers, decoders, registers, arithmetic circuits, counters, memory arrays, logic arrays.
Building blocks demonstrate hierarchy, modularity, and regularity:
  Hierarchy of simpler components.
  Well-defined interfaces and functions.
  Regular structure easily extends to different sizes.

## Slide 4: 1-Bit Adders Revisited …
A | B | Sum | Cout
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
Inputs
Outputs
S
B
A
+
Cout
Half Adder
S = A + B
Cout = AB
S
B
A
+
Cout
Cin
Cin | A | B | Sum | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
Inputs
Outputs
Full Adder
S = A + B + Cin
Cout = AB + ACin + BCin
Notes: We are revisiting material from lecture 12 – combinational logic.

## Slide 5: Multi-Bit Adders
Types of carry propagate adders (CPAs):
  Ripple-carry (slow) [See lecture 12]
  Carry-lookahead (fast)
Carry-lookahead adders faster for large adders but require more hardware.
  Usually arranged in blocks of 4.

## Slide 6: Ripple Carry Adder
Chain 1-bit adders together
Carry ripples through entire chain.
Disadvantage: slow
Ripple Carry Adder delay:
  tripple = N tFA where tFA is the delay of a full adder
WHY? Sum of the MSB is only available after the carry signal has rippled through the adder from the least significant stage to the most significant stage. As a result, the final sum and carry bits will be valid after a considerable delay…
Notes: Why is a ripple carry slow?
A ripple-carry adder works in the same way as pencil-and-paper methods of addition. Starting at the rightmost (least significant) digit position, the two corresponding digits are added and a result obtained. It is also possible that there may be a carry out of this digit position. Accordingly all digit positions other than the rightmost need to take into account the possibility of having to add an extra 1, from a carry that has come in from the next position to the right.
This means that no digit position can have an absolutely final value until it has been established whether or not a carry is coming in from the right.

## Slide 7: Carry Lookahead Adder
The carry lookahead adder (CLA) solves the carry delay problem by calculating the carry signals in advance, based on the input signals.
It is based on the fact that a carry signal will be generated in two cases:
  (1) when both bits A and B are 1, or
  (2) when one of the two bits is 1 and the Cin is 1.
Ci+1 = AiBi + (Ai + Bi)Ci
Notes: NOTE
In the case of binary addition, A+B propagates if and only if at least one of A or B is 1 [case (2) in the slide above]. Often a slightly different definition of propagate is used. By this definition A + B is said to propagate if the addition will carry whenever there is an input carry, but will not carry if there is no input carry - hence the use of XOR in the equation above.
Fortunately, due to the way generate and propagate bits are used by the carry lookahead logic, it doesn't matter which definition is used.
See also the circuit diagram on the next slide, which makes it clear why XOR used.

## Slide 8: Carry Lookahead Adder (CLA)
The two equations on the last slide can be written in terms of two new signals Pi and Gi - shown in the full adder circuit.
  Gi = carry generate term
  Pi = carry propagate term
The carry-lookahead adder calculates one or more carry bits before the sum, which reduces the wait time to calculate the result of the larger value bits.
Si
Ci
Ai
Bi
Ci+1
Pi
Gi
Gi = AiBi
Pi = Ai + Bi
Ci+1 = Gi + PiCi
Notes: NOTE
Notice that the generate and propagate terms only depend on the input bits !

## Slide 9: Carry Lookahead Adder (CLA)
A block generates a carry if the most significant column generates a carry, or if the most significant column propagates a carry and the previous column generated a carry and so forth
  G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 )
A block propagates a carry if all the columns in the block propagate the carry:
  P3:0 = P3P2 P1P0

## Slide 10: Carry Lookahead Adder (CLA)
Using the block generate and propagate signals, we can quickly compute the carry out of the block, Ci, using the carry in to the block, Cj
  Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2Gj )
  Pi:j = PiPi-1 Pi-2Pj
  Ci = Gi:j + Pi:j Ci-1

## Slide 11: 32-bit CLA with 4-Bit Blocks
Each 4-bit block contains:
  4-bit ripple carry-adder
  Lookahead logic to compute the carry out of the block given the carry in
Lookahead logic

## Slide 12: CLA Delay
For N-bit CLA with k-bit blocks: tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA tpg : delay to generate all Pi, Gi tpg_block : delay to generate all Pi:j, Gi:j tAND_OR : delay from Cin to Cout of final AND/OR gate in k-bit CLA block
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16
tpg
tpg_block
ktFA
tAND_OR
Notes: N = number of bits for the entire carry
K = number of bits in the block
Tpg is the delay of the individual generate/propagate gates (a single AND or OR gate)
Tpg_block is the delay to find the generate/propagate signals for the whole 4-bit block

## Slide 13: Ripple vs Carry Lookahead
Compare the delays of a 32-bit ripple-carry adder and a 32-bit carry-lookahead adder with 4-bit blocks. Assume that each 2-input gate delay is 100ps and that a full adder delay is 300ps.
Carry Lookahead Adder:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
tpg = 100ps
tpg_block = 6 x 100ps = 600ps
tAND_OR = 2 x 100ps = 200ps
The propagation delay of the 32-bit carry-lookahead adder =
100ps + 600ps + (32/4 – 1) x 200ps + (4 x 300ps) = 3.3ns
Ripple Carry Adder:
Propagation delay of the 32-bit ripple carry adder:
tripple = NtFA = 32(300 ps) =9.6ns
Carry Lookahead is significantly faster!