## Slide 1
Digital Design and Computer Architecture, 2nd Edition
Chapter 5
David Money Harris and Sarah L. Harris

## Slide 2
Digital building blocks:
  Gates, multiplexers, decoders, registers, arithmetic circuits, counters, memory arrays, logic arrays
Building blocks demonstrate hierarchy, modularity, and regularity:
  Hierarchy of simpler components
  Well-defined interfaces and functions
  Regular structure easily extends to different sizes
Introduction

## Slide 3
Subtracter
Adder can add positive and negative numbers using two’s complement representation.
Subtraction: inverting the bits and adding 1.
Flipping the sign of a two’s complement number is done by inverting the bits and adding 1.

## Slide 4
Comparator: Equality
A comparator determines whether two binary numbers are equal or if one is greater or less than the other.
An equality comparator produces a single output indicating whether A is equal to B

## Slide 5
Comparator: Less Than
Magnitude comparison is done by computing A - B and looking at the sign (most significant bit) of the result.
If the result is negative (i.e., the sign bit is 1), then A is less than B. otherwise A is greater than or equal to B

## Slide 6
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
Arithmetic/Logic Unit (ALU)
An ALU combines a variety of mathematical and logical operations into a single unit. (addition, subtraction, magnitude comparison, AND, OR operations)
A control signal F specifies which function to perform

## Slide 7
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
ALU Design
BB

## Slide 8
ALU Design
F2:0 | Function
000 | A & B
001 | A ¦ B
010 | A + B
011 | not used
100 | A & ~B
101 | A ¦ ~B
110 | A - B
111 | SLT
BB is either B or ~B, depending on F2.
If F1:0 = 00, the output multiplexer chooses A AND BB.
If F1:0 = 01, the ALU computes A OR BB.
If F1:0 = 10, the ALU performs addition or subtraction.
If F2 = 0, the ALU computes A+B,
If F2 = 1, the ALU computes A + ~B + 1 = A – B.
When F2:0 = 111, the ALU performs the set if less than (SLT) operation.
When A < B, Y =1, otherwise Y = 0.
i.e., Y is set to 1 if A is less than B.

## Slide 9
ALU Design
The zero extend unit produces an N-bit output by concatenating its 1-bit input with 0’s in the most significant bits.
The sign bit (the N-1th bit) of S is the input to the zero extend unit.
BB

## Slide 10
Configure 32-bit ALU for SLT operation.
Suppose A = 25 and B = 32
Show the control signals and output Y.
Example 5.3 - Set Less Than (SLT)
BB

## Slide 11
Configure 32-bit ALU for SLT operation: A = 25 and B = 32
  A < B, so Y should be 32-bit representation of 1 (0x00000001)
  F2:0 = 111
    F2 = 1 (adder acts as subtractor), so 25 - 32 = -7
    -7 has 1 in the most significant bit (S31 = 1)
    F1:0 = 11 multiplexer selects Y = S31 (zero extended) = 0x00000001.
Example 5.3 - Set Less Than (SLT)
BB

## Slide 12
Shifters and rotators move bits and multiply or divide by powers of 2.
Logical shifter: shifts value to left (LSL) or right (LSR) and fills empty spaces with 0’s
  Ex: 11001 >> 2 =
  Ex: 11001 << 2 =
Arithmetic shifter: same as logical shifter. But on right shift, fills empty spaces with the old most significant bit (msb). Useful for multiplying and dividing signed numbers
  Ex: 11001 >>> 2 =
  Ex: 11001 <<< 2 =
Rotator: rotates bits in a circle, such that bits shifted off one end are shifted into the other end
  Ex: 11001 ROR 2 =
  Ex: 11001 ROL 2 =
Shifters and Rotators

## Slide 13
Logical shifter:
  Ex: 11001 >> 2 = 00110
  Ex: 11001 << 2 = 00100
Arithmetic shifter:
  Ex: 11001 >>> 2 = 11110
  Ex: 11001 <<< 2 = 00100
Rotator:
  Ex: 11001 ROR 2 = 01110
  Ex: 11001 ROL 2 = 00111
Shifters

## Slide 14
Shifter Design
(a) Shift left (b) logical shift right (c) arithmetic shift right
An N-bit shifter can be built from N N:1 multiplexers

## Slide 15
Shifter Design
Shift left
A left shift by N bits multiplies the number by 2N.
For example, 0000112 << 4 = 1100002 is equivalent to 310 x 24 = 4810

## Slide 16
Shifter Design
An arithmetic right shift by N bits divides the number by 2N.
For example, 111002 >>> 2 = 111112 is equivalent to -410 ÷ 22 = -110.

## Slide 17
A << N = A × 2N
  Example: 00001 << 2 =
  Example: 11101 << 2 =
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 =
  Example: 10000 >>> 2 =
Shifters as Multipliers, Dividers

## Slide 18
A << N = A × 2N
  Example: 00001 << 2 = 00100 (1 × 22 = 4)
  Example: 11101 << 2 = 10100 (-3 × 22 = -12)
A >>> N = A ÷ 2N
  Example: 01000 >>> 2 = 00010 (8 ÷ 22 = 2)
  Example: 10000 >>> 2 = 11100 (-16 ÷ 22 = -4)
Shifters as Multipliers, Dividers

## Slide 19
Numbers we can represent using binary representations
  Positive numbers
    Unsigned binary
  Negative numbers
    Two’s complement
    Sign/magnitude numbers
What about fractions?
Number Systems

## Slide 20
Two common notations:
  Fixed-point: binary point fixed
  Floating-point: binary point floats to the right of the most significant 1
Numbers with Fractions

## Slide 21
6.75 using 4 integer bits and 4 fraction bits:
  Binary point is implied
  The number of integer and fraction bits must be agreed upon beforehand
Fixed-Point Numbers

## Slide 22
Represent 7.510 using 4 integer bits and 4 fraction bits.
Fixed-Point Number Example

## Slide 23
Represent 7.510 using 4 integer bits and 4 fraction bits.
  7 = 0111
  0.5 = 2-1
  Thus, 7.510 = 0111 1000
Fixed-Point Number Example

## Slide 24
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  Two’s complement:
Signed Fixed-Point Numbers

## Slide 25
Representations:
  Sign/magnitude
  Two’s complement
Example: Represent -7.510 using 4 integer and 4 fraction bits
  Sign/magnitude:
  11111000
  Two’s complement:
  1. +7.5: 01111000
  2. Invert bits: 10000111
  3. Add 1 to lsb: + 1
  10001000
Signed Fixed-Point Numbers

## Slide 26
Example 5.4
Compute 0.75 + (–0.625) using fixed-point numbers

## Slide 27
Example 5.4
Compute 0.75 + (–0.625) using fixed-point numbers
First convert 0.625 to fixed-point binary notation.
0.625 ≥ 2-1, so there is a 1 in the 2-1 column, leaving 0.625 – 0.5 = 0.125.
Because 0.125 < 2-2, there is a 0 in the 2-2 column
Because 0.125 ≥ 2-3, there is a 1 in the 2-3 column, leaving 0.125 – 0.125 = 0.
Thus, there must be a 0 in the 2-4 column. Putting this all together, 0.62510 = 0000.10102.
2-1 = 0.5
2-2 = 0.25
2-3 = 0.125
2-4 = 0.0625

## Slide 28
Use two’s complement representation for signed numbers so that addition works correctly.
Note that the leading 1 in the binary fixed-point addition of Figure (a) is discarded from the 8-bit result.
Example 5.4

## Slide 29
Exercise 5.25 (b)
Express 42.312510 in 16-bit fixed point sign/magnitude format with eight integer bits and eight fraction bits.

## Slide 30
Exercise 5.25 (b)
Express 42.312510 in 16-bit fixed point sign/magnitude format with eight integer bits and eight fraction bits.
4210 = 0010 10102
0.3125 < 0.5, so there is a 0 in the 2-1 column
0.3125 ≥ 0.25, so there is a 1 in the 2-2 column, leaving 0.3125 – 0.25 = 0.0625
0.0625 ≥ 0.0625, so there is a 1 in the 2-4 column
Thus, 0.3125 = 0101 0000
42. 3125 = 0010 1010. 0101 0000